#### Customer Specification

| Slim | Slim with GPS |
| --- | --- |

DIN horizontal

Motorola offers this information to our customer as a service to assist in the applications and engineering efforts with our products. Motorola is basing this information only on what has been provided specifically to Motorola by our customer.  Motorola has not undertaken any independent search for additional relevant information, including any information that may be in our customer’s possession.   Furthermore, system validation of this Motorola product within a larger electronic system remains the responsibility of our customer or our customer’s system integrator.  All specifications are subject to change.

| Physical |  |
| --- | --- |
| Form factor: | Enclosed, DIN Horizontal PCB or Enclosed GPRS/GPS |
| Size: | g18 (GPRS) DV Slim: 44.29x88.45x10.4mm (see drawings in this spec) g18 (GPRS) DVG with GPS: 44.54x88.45x17.6mm g18 (GPRS) DV DIN: 40x80.2x7.5 mm |
| Mounting: | Four 2.43mm Ø holes provided on non DIN models |
| Weight: | g18 (GPRS) DV Slim: 35.5g g18 (GPRS) (GPRS) DVG with GPS: 49g g18 (GPRS) DV DIN: 22g |
| Volume: | g18 (GPRS) DV Slim: 36.8 cc g18 (GPRS) DVG with GPS: 57.0 cc g18 (GPRS) DV DIN: 24.1 cc |
| Housing material: | Plastic housing PC/ABS |
| Interface connector: | g18 (GPRS) DV Slim/ DVG: | 36 pin ZIF socket @ 0.5mm pitch ELCO #04-6240-036-800 |
|  | g18 (GPRS) DV Horizontal Board Only: | 28 pin dual in line pin socket @1.27 pitch (SAMTEC # CLP-114-02-L-D) and 36 pin ZIF socket |
| RF output connector: | MMCX Jack (female) 50( GSM and GPS Mating connectors Plug (Male) Coax Huber-Shuhner Johnson Components RG178 11-MMCX-50-1-1 135-3302-001 RG316 11-MMCX-50-2-3 135-3403-001 |
| Environmental |  |
| Operational temperature: | -30 to +60 degrees C |
| Storage temperature: | -40 to +85 degrees C |
| Shock: | 20 g’s with 11 millisecond duration, 20 impacts in three mutually perpendicular planes |
| Vibration: | IS-19: 1.5g acceleration, 5 to 500 Hz @ 0.1 octave/minute in three mutually perpendicular planes |
| Performance |  |
| Operating systems | GSM 900MHz, DCS 1800MHz, PCS 1900MHz. |
| Voltage:③ | 3.0 to 6V measured at the I/O connector during the transmit slot (576us out of 4.6ms) |
| Current: | =7.2 +/- 0.5 mA @ DRX 2 Stand by (sleep) =3.5 +/- 0.5 mA @ DRX 9 Stand by (sleep) < 150uA off current Tx Current @ 900 MHz 300mA avg. in call at power level 5 (max. 350 mA @ 900 MHz) 1.2 A peak @ 217 Hz at power level 5 (max. 1.8A@ 900 MHz ) |
| Power out: | GSM – Power levels #19 to 5, 5dBm to 33dBm per ETSI. DCS – Power levels # 15 to 0, 0dBm to 30 dBm per ETSI. PCS – Power levels # 15 to 0, 0 dBm to 30 dBm per FCC. |
| SIM Card Reader:① | Options: | 1. Internal - chip SIM CR 3/5V SIM 2. External - Local interface 3/5 SIM 3. External - Remote interface (DSC interface) 5V only |
| Interface: | Options: | 9 line RS232 Serial Asynchronous full flow control , 3V logic level (DCE flow direction) Vih 2.0 V min, 5.5 V max Vil 0.8 V max Voh 2.5 V min @100 uA Vol 0.2 V max @ 100 uA Wizard application SW, which runs on PC, used to activate PDP context (GPRS only) Motorola Proprietary DSC Bus GPS interface (TxD, RxD, 1PPS, RTCM and Antenna voltage), on Slim-GPS model. |

| Host Protocol: | CSD mode: AT commands including GSM 07.07,GSM 07. 05 (see Developers manual for specific AT commands supported) GRRS mode: AT commands per standard for GSM 07.60 and 07.07 ver 7.5.0. (see Developers manual for specific AT commands supported) |
| --- | --- |
| Data: | RS232 CSD mode GPRS mode | RS232 port up to 57.6kbps. The default is set at 9.6 kbps with auto-baud detection active up to 19.2 kbps. For rates above 19.2 kbps the baud rate can be set by At command up to 57.6 kbps, which needs to be reset after each power cycle. Over the air rate depending on network, 9.6 kbps max) Circuit Switched Data Over the air data rate depends on coding schemes (CS1-CS4), but limited to 57.6 kbps. GPRS packet data (SMG31) Class B (only when a handset is used), multi slot class 1, 2 and 4, 1X (uplink)/1X (downlink) or 1X (uplink)/2X (downlink) or 1X (uplink)/3X (downlink) coding schemes CS1 to CS4 |
| SMS: | Send and receive (PDU and block mode per GSM 07.05) |
| Voice Call: | Supported I/O with external H/SET |
| Audio: | Analog - Full duplex I/O on interface connector Digital - Motorola Proprietary DSC Bus Echo canceling activated by AT for HandsFree Audio applications (analog only) |
| GPS: | Independent GPS receiver (GPS model only) GPS (TXD, RXD, 1PPS, RTCM, Antenna Voltage) Functions are available on the ZIF and DIN header/socket connector at 3V logic levels. 12 parallel channel L1 1574,42 MHz Code plus carrier tracking (carrier aided tracking) Positional accuracy: 100 meters 2dRMS with SA as per DoD specifications, less than 25 meters SEP without SA Additional specifications available on request |

Interface connector,  36 pin description Slim , Slim with GPS and DIN Horizontal

| Pin # | Function | Pin # | Function |
| --- | --- | --- | --- |
| 1 | TX Enable | 19 | SIM CR I/O Data |
| 2 | RXD Uart 2 (GPS RXD on GPS models) | 20 | SIM CR Clock |
| 3 | TRD Uart 2 (GPS TXD on GPS models) | 21 | TS (Turn on/stand by) ⑤ |
| 4 | RS232 – TXD ⑦ | 22 | DSC - Enable |
| 5 | RS232 – RXD⑧ | 23 | DSC - Downlink |
| 6 | RS232 – DTR | 24 | DSC - Uplink |
| 7 | RS232 – DCD for CSD call/PDP context indicator ⑩ | 25 | Analog Audio GND |
| 8 | RS232 – RTS | 26 | GND |
| 9 | RS232 – CTS | 27 | GND |
| 10 | RS232 – DSR | 28 | GND |
| 11 | RS232 – RI | 29 | GND |
| 12 | Man test | 30 | Vcc (3.0 – 6 Vdc) |
| 13 | Analog Audio In | 31 | Vcc (3.0 – 6 Vdc) |
| 14 | Analog Audio Out and Power on/off ⑥ | 32 | Vcc (3.0 – 6 Vdc) |
| 15 | Wake up/GPRS coverage indicator ⑨ | 33 | Vcc (3.0 – 6 Vdc) |
| 16 | Input I/O (custom definition) & SIM CR DET ④ | 34 | GPS Ant. PWR (3/5 Vdc) |
| 17 | SIM CR Vcc (3/5Vdc) | 35 | RX for differential GPS RTCM |
| 18 | SIM CR Reset (RST) | 36 | GPS 1 pps |

Functions on pin numbers 2,3,34,35 and 36 on units with GPS only

### Slim, Slim with GPS and DIN horizontal models Functions available on 36 pin ZIF

| VCC input | 3.0 to 6Vdc |
| --- | --- |
| Full RS232 - 9 pins | TXD, RXD, RTS,CTS, DSR, DTR,DCD RI at 3V levels |
| External SIM connections | SIM Clock, SIM reset, SIM I/O, SIM VCC,SIM PD |
| DSC bus | DSC_EN, Downlink, Uplink Motorola proprietary BUS |
| Audio In/Out | Audio out and On/Off in the same pin, audio in Signal and analog ground |
| Man_Test line | Used to detect standard Motorola accessories |
| TS line (mobport). | Used to turn on the radio when Vcc is applied |
| TX_EN line | This line is an indication when the radio is transmitting (Open drain) |
| GPS (GPS option only) | TXD & RXD in 3V levels, 1PPS, RTCM, Antenna power. RXD and TXD lines are at 3V levels. The GPS receiver is the Motorola M12 |
| RXD and TXD on Uart 2 | Reserved for future feature |

# Interface connector,  28 pin description DIN horizontal

| Pin # | Function | Pin # | Function |
| --- | --- | --- | --- |
| 1 | Vcc (3.0 – 6) Vdc | 15 | RXD Uart 2 |
| 2 | Vcc (3.0 – 6)Vdc | 16 | TXD Uart 2 |
| 3 | SIM CR I/O Data | 17 | Analog Audio GND |
| 4 | SIM CR Reset (RST) | 18 | Analog Audio Out and Power on/off ⑥ |
| 5 | SIM CR Vcc (3/5Vdc) | 19 | Analog Audio In |
| 6 | SIM CR DET | 20 | DSC - Enable |
| 7 | RS232 – DTR | 21 | RS232 - DSR |
| 8 | TS (Turn on/stand by) ⑤ | 22 | DSC - Downlink |
| 9 | Man test | 23 | DSC - Uplink |
| 10 | Wake up/GPRS coverage indicator ⑨ | 24 | SIM CR Clock |
| 11 | GND | 25 | RS232 – TXD ⑦ |
| 12 | GND | 26 | RS232 - RXD ⑧ |
| 13 | RS232 – RI | 27 | RS232 - CTS |
| 14 | RS232 – DCD for CSD call/PDP context indicator ⑩ | 28 | RS232 - RTS |

### DIN  horizontal Functions available on 28 pin ZIF

| VCC input | 3.0 to 6Vdc |
| --- | --- |
| Full RS232 - 9 pins | TXD, RXD, RTS,CTS, DSR, DTR,DCD RI at 3V levels |
| External SIM connections | SIM Clock, SIM reset, SIM I/O, SIM VCC,SIM PD |
| DSC bus | DSC_EN, Downlink, Uplink Motorola proprietary BUS |
| Audio In/Out | Audio out and On/Off in the same pin, audio in Signal and analog ground |
| Man_Test line | Used to detect standard Motorola accessories |
| TS line (Turn on / Stand by | Used to turn on the radio when Vcc is applied |
| TX_EN line | This line is not provide in the DIN models |
| RXD and TXD on Uart 2 | Reserved for future feature |

Pin 14 on 36 pin connector and  pin 18 on 28 pin connector Definition  (Audio Out, Rec audio)

- Freq. Response:  max +/- 3db from 300 to 3000 Hz

- Output impedance:  max. 1000 (

- Distortion:  max. 5%

- Audio level:  max 1.2V ptp

- Headset ②

Pin 13 on 36 pin connector and  pin 19 on 28 pin connector Definition   (Audio In, Transmit audio)

------------------------

- Freq. response: max  +_3dB from 300 to 3000 Hz

- Input impedance:  10K (

- Distortion: max. 5%

- Input level: max. 500 mVptp.

- Headset ②

Footnotes:

| ① | One SIM card can be used with option 1 and 2. With option 3 two SIM cards can be in the system. When connecting the remote card reader to evaluation board use handset connector. |
| --- | --- |
| ② | When using Motorola head set SYN4937A and SYN6962A; evaluation board demonstrates this implementation. |
| ③ | It is recommended that a 1000 uF capacitor be placed across GND and VCC as close as possible to the flex cable on versions with a housing or the 28 way connector on the DIN version. This will prevent Vcc drop during peak current which has a 543(s duration every 4.3ms due to GSM power pulses. Voltage must not drop below 3.0vdc or the performance of the module will be degraded. |
| ④ | Custom definition will be considered for specific applications. |
| ⑤ | Logic high will turn unit on, logic low put the unit into stand by mode. You must turn unit on before placing unit into standby mode. An alternate way to power the radio on is by using the On/Off pin |
| ⑥ | The Audio Out line is used to send out the detected audio and as a toggle On/Off pin. |
| ⑦ | Data received by g18 (DCE flow) |
| ⑧ | Data sent from g18 (DCE flow) |
| ⑨ | Wake up line is bi – directional When going from non GPRS coverage to GPRS coverage, a negative pulse will be generated on this line When the g18 wants to send data to the DTE (host), a negative pulse will be generated on this line When DTE (host) wants to send data (while the g18 is in sleep mode) it can send a wake up to the g18 |
| ⑩ | GPRS PDP context active – DCD line will be active (low) GPRS PDP context not active – DCD line will be inactive (high) |

Remarks

- Revision notes are contained in the developers manual.

- Evaluation kit is available for developer integration.

g18 (GPRS) DV Slim

g18 (GPRS) DV Slim with GPS

g18 (GPRS) DV DIN Horizontal

g18 Sales model table

| Language pack Description | Language 01 Western Europe | Language 03 GSM 1900 NA | Language 06 Nordic | Language 07 East Europe | Language 08 Mid East | Language 08 Mid East Arabic |
| --- | --- | --- | --- | --- | --- | --- |
| g18 DV slim | SE2836xF5Z8 | SE2836xF5Z6 | SE2836xF5Y5 | SE2836xF5Y6 | SE2836xF5Z5 | SE2841xF5Z5 |
| g18 DV slim w/GPS | SE2837xF5Z8 | SE2837xF5Z6 | SE2837xF5Y5 | SE2837xF5Y6 | SE2837xF5Z5 | SE2842xF5Z5 |
| g18 DV DIN Horz | SE2838xF5Z8 | SE2838xF5Z6 | SE2838xF5Y5 | SE2838xF5Y6 | SE2838xF5Z5 | SE2843xF5Z5 |
| Languages |  |  |  |  |  |  |
| Arabic |  |  |  |  | X | X |
| Bulgarian |  |  |  | X |  |  |
| Chinese-Complex |  |  |  |  |  |  |
| Chinese-Simplified |  |  |  |  |  |  |
| Croatian |  |  |  | X |  |  |
| Czech |  |  |  | X |  |  |
| Danish | X |  | X |  |  |  |
| Dutch | X |  |  |  | X | X |
| English | X |  | X | X | X | X |
| English-American |  | X |  |  |  |  |
| Estonian |  |  | X |  |  |  |
| Finnish | X |  | X |  |  |  |
| French | X |  |  |  | X | X |
| French-Canadian |  | X |  |  |  |  |
| German | X | X |  | X | X | X |
| Greek | X |  |  |  | X | X |
| Hebrew |  |  |  |  | X | X |
| Hungarian | X |  |  |  |  |  |
| Indonesian-Bahasa |  |  |  |  |  |  |
| Italian | X | X |  |  | X | X |
| Latvian |  |  | X |  |  |  |
| Lithuanian |  |  | X |  |  |  |
| Norwegian | X |  | X |  |  |  |
| Polish |  |  |  | X |  |  |
| Portuguese | X | X |  |  |  |  |
| Romanian |  |  |  | X |  |  |
| Russian |  |  | X |  | X | X |
| Serbian |  |  |  | X |  |  |
| Slovak |  |  |  | X |  |  |
| Slovenian |  |  |  | X |  |  |
| Spanish | X |  |  |  |  |  |
| Spanish-American |  | X |  |  |  |  |
| Swedish | X |  | X |  |  |  |
| Thai |  |  |  |  |  |  |
| Turkish | X |  |  |  | X | X |
| Ukrainian |  |  | X |  |  |  |
| Vietnamese w/tonal marks |  |  |  |  |  |  |

Note:  	GPS models check with your sales representative

“x” indicates version level

The data module will display local languages prompts either on a handset or developed MMI.  Even if you are not using this feature you must select a model within a language pack as shown above when ordering.  Default language is always set to English.

# Text boxes

Keep out