DSR.COM


This is a very specific diagnostic test which tries to locate
the source of a DSR short.  Run this test if the TMT test says the DTR-DSR test
passed but there was a CHARIN failure on the string test.  This happens if 
there is a short between the DSR and DTR pins.

Run the DSR test specifying the COM port you wish to test:

        A>DSR COM2

You must run the test twice - first with the cable plugged into the COM port 
and then without the cable.  The test will look for a short and if the short 
happens only when the cable is attatched then the short must be in the cable, 
otherwise it must be in the COM port.