ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
         º                 ****   NOTE   ****                    º 
         º                                                       º
         º  These programs are included as utilities to The $25  º
         º  Network which is a copyrighted, commercial program.  º
         º  Nothing on this disk is shareware or  public domain  º
         º  and  may  not  be  copied and distributed to anyone  º
         º  without the written permission of Information Modes. º 
         ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼



                            COMIRQ.COM

        This utility allows you to turn on or turn off the interrupt request 
line (IRQ) on a specific COM port.  The PC/XT/AT hardware was not designed to 
permit interrupt lines to be shared.  Since COM1 and COM3 share the same 
interrupt, and COM2 and COM4 share the other communications interrupt,  it is 
possible for a COM port to get in the way of another COM port's use of its IRQ 
line.  COMIRQ will disable (tri-state) a COM port's IRQ line to permit another 
COM port to use it.  One likely use is with PROCOMM.  If you have the network 
running on COM3 and then load PROCOMM on COM1 you may find either PROCOMM does 
not work or the network does not work when you exit PROCOMM.  Run COMIRQ to 
disable the network's COM port IRQ line before loading PROCOMM, then disable 
PROCOMM's COM port when you exit it, remembering to re-enable the network's COM 
port.


EXAMPLE OF USE:
---------------

        COMIRQ COM3 IRQ=OFF

or,
        COMIRQ COM1 IRQ=ON

or,
        COMIRQ COM:3E8 IRQ=OFF

or,
        COMIRQ COM:3E8 IRQOFF

or,
        COMIRQ COM:3E8 IRQON


etc...