FOR OFFICIAL USE ONLY

CROWN COPYRIGHT RESERVED

The information within this publication

is released by the UK Government to the

recipient in accordance with the

Conditions of Release given at

Page/Frame …..

TRUCK, 1 TONNE, 4 x 4 ROVER (V8)

(ALL VARIANTS)

MAINTENANCE SCHEDULE

BY COMMAND OF THE DEFENCE COUNCIL

Sponsor:

DGEME(A)/125/14/45 EME 7b

File ref:

Publications Authority:

Vehs & Wpns Br REME

Ministry of Defence						Project No: 71311

CONDITIONS OF RELEASE

- This information is released by the UK Government for defence purposes only.

- This information must be accorded the same degree of security protection as that accorded thereto by the UK Government.

- This information may be disclosed only within the Defence Departments of the recipient government, except as otherwise authorised by the Ministry of Defence (Army).

- This information may be subject to privately owned rights.

AMENDMENT RECORD

| Amdt | Incorporated by | Date |  | Amdt | Incorporated by | Date |
| --- | --- | --- | --- | --- | --- | --- |
| 1 |  |  |  | 32 |  |  |
| 2 |  |  |  | 33 |  |  |
| 3 |  |  |  | 34 |  |  |
| 4 |  |  |  | 35 |  |  |
| 5 |  |  |  | 36 |  |  |
| 6 |  |  |  | 37 |  |  |
| 7 |  |  |  | 38 |  |  |
| 8 |  |  |  | 39 |  |  |
| 9 |  |  |  | 40 |  |  |
| 10 |  |  |  | 41 |  |  |
| 11 |  |  |  | 42 |  |  |
| 12 |  |  |  | 43 |  |  |
| 13 |  |  |  | 44 |  |  |
| 14 |  |  |  | 45 |  |  |
| 15 |  |  |  | 46 |  |  |
| 16 |  |  |  | 47 |  |  |
| 17 |  |  |  | 48 |  |  |
| 18 |  |  |  | 49 |  |  |
| 19 |  |  |  | 50 |  |  |
| 20 |  |  |  | 51 |  |  |
| 21 |  |  |  | 52 |  |  |
| 22 |  |  |  | 53 |  |  |
| 23 |  |  |  | 54 |  |  |
| 24 |  |  |  | 55 |  |  |
| 25 |  |  |  | 56 |  |  |
| 26 |  |  |  | 57 |  |  |
| 27 |  |  |  | 58 |  |  |
| 28 |  |  |  | 59 |  |  |
| 29 |  |  |  | 60 |  |  |
| 30 |  |  |  | 61 |  |  |
| 31 |  |  |  | 62 |  |  |

CONTENTS

Preliminary material									Page

No

Title Page									(i)

Conditions of release								(ii)

Amendments record								(iii)

Contents (this page)								(iv)

Preface										(iv)

Associated publications								(iv)

Warnings and Cautions								(v)

## Para

MAINTENANCE SCHEDULE							 1

1 Authority

2 Responsibilities

5 Inspections and examinations

7 Records

8 Serial numbers

9 Abbreviations

## Table

1 Equipment applicability							 2

2 Fuels, lubricants and associated products					 3

3 Equipment data								 4

4 Drivers/operator maintenance							5-6

5 Periodic maintenance								7-11

6 Out of use maintenance							 12

## Fig

1 Lubrication diagram								 12

### PREFACE

1 Comments on this publication are to be forwarded in accordance with AESP 0100-P-011-013 to Vehicles and Weapons Branch REME, Chobham Lane, Chertsey, Surrey KT16 0EE.

WARNINGS

- THE HANDLING OF FUELS, LUBRICANTS AND ASSOCIATED PRODUCTS IS HAZARDOUS REFER TO LOCAL UNIT SAFETY PROCEDURES, INSTRUCTIONS ON THE CONTAINERS AND OTHER RELAVENT REGULATIONS FOR FULL SAFETY PROCEDURES.

MINIMUM PRECAUTIONS AFTER USE IS TO WASH AFFECTED SKIN AREAS WITH SOAP AND WATER.

THE USE OF BARRIER CREAM IS RECOMMENDED.

- FLUID AL 39 IS BOTH TOXIC AND HAZARDOUS

- FLUID AL 11 IS HIGHLY INFLAMMABLE

THE PREPARATION OF THE FLUID IS TO BE CARRIED OUT IN THE OPEN AWAY FROM NAKED FLAMES

- THIS VEHICLE HAS PERMANENT 4 WHEEL DRIVE. UNDER NO CIRCUMSTANCES SHOULD ANY TEST BE CARRIED OUT THAT INVOLVES JACKING UP ONE PAIR OF WHEELS AND RUNNING THE VEHICLE IN GEAR.

- ON NO ACCOUNT SHOULD MORE THAN THREE ATTEMPTS BE MADE TO START THE HEATER, IF IT FAILS TO START BY THE THIRD ATTEMPT, REPORT TO REME. DO NOT OPERATE THE HEATER IN AN ENCLOSED AREA.

- HIGH PRESSURE OXYGEN SUPPLY, DO NOT ALLOW GREASE, OIL OR NAKED FLAMES NEAR OXYGEN EQUIPMENT.

CAUTIONS

- CONTINUOUS BUBBLES OR FOAM INDICATE A LOW LEVEL OF REFRIGERANT AND/OR POSSIBLE SYSTEM LEAK. TO PREVENT DAMAGE TO COMPRESSOR, SWITCH OFF SYSTEM.

- DO NOT REMOVE THE ENGINE OIL FILTER WHILST THE SUMP IS DRAINED (THE OIL PUMP IS NOT SELF-PRIMING)

### ASSOCIATED PUBLICATIONS

JSP 341						Road Transport Regulations

JSP 351						“MT Drivers’ Handbook”

Army Code 22260				User Handbook

Army Code 24044				User Handbook (Ambulance)

Q 050-059					Emer Whld Veh.

Q 052/1 Ambulance				Emer Whld Veh.

### MAINTENANCE SCHEDULE

## Authority

- This Maintenance Schedule is the authority for carrying out all servicing tasks on the subject equipment.

## Responsibilities

- The unit commander is responsible for ensuring that the operations detailed in this schedule are properly carried out. He may order any operation to be carried out more frequently than is specified if the conditions under which his equipments are operating render it necessary. He should consult his REME advisor before ordering such changes.

- The unit commander may adjust the specified servicing intervals by plus or minus 10 per cent to suit local circumstances.

- The operator/driver is responsible for ensuring the equipment is fit for task. If the mechanical fitness is in doubt, the equipment is not to be used until advice has been sought.

## Inspections and examinations

- The unit commander is advised to arrange inspections to be carried out on receipt of the equipment and thereafter in accordance with JSP 341 Chap 16 para 16.454.

- Examinations are carried out by REME in accordance with AGAI Vol 4 para 142.031-142.036.

## Records

- Servicings and inspections are to be recorded in the equipment documents.

## Serial numbers

- Serial numbers left blank may be taken up by amendment action at a later date.

## Abbreviations

- VM – Vehicle Mechanic

TABLE 1 – EQUIPMENT APPLICABILITY

| Ser | Equipment Code No | Designation |
| --- | --- | --- |
| (1) | (2) | (3) |
| 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 | 1825-0750 1825-5750 1831-0750 1832-0750 1832-5750 1833-0750 1833-5750 1834-0750 1834-5750 1840-0750 1840-5750 1850-0750 1850-5750 1054-0750 1054-5750 | Truck General Service w/winch 1 tonne 4 x 4. Truck General Service w/winch 1 tonne 4 x 4, LHD. Truck General Service 24V, signals w/winch 1 tonne 4 x 4. Truck General Service w/winch, FFR 1 tonne 4 x 4. Truck General Service w/winch, FFR 1 tonne 4 x 4, LHD. Truck General Service 24V, Launcher towing Rapier. Truck General Service 24V, Launcher towing Rapier w/winch 1 tonne 4 x 4, LHD. Truck General Service 24V, signals 1 tonne 4 x 4. Truck General Service 24V, signals 1 tonne 4 x 4, LHD. Truck General Service, 1 tonne 4 x 4. Truck General Service, 1 tonne 4 x 4, LHD. Truck General Service, FFR 1 tonne 4 x 4. Truck General Service, FFR 1 tonne 4 x 4, LHD. Ambulance 4 Str, 4 x 4. Ambulance 4 Str, 4 x 4, LHD. |

TABLE 2.0 – FUELS, LUBRICANTS AND ASSOCIATED PRODUCTS

Notes…

- Oil changes at the –15 degree C point shall only be made on the advice of the local REME adviser.  Changes of grade will normally be recommended when the ambient temperature is expected to fall below –15 degrees C for more than five hours per day. Special instructions will apply if the engine has been ‘winterised’.

- All fluid capacities are to be checked with the vehicle on level ground and unladen whenever possible. The capacities listed are to be used as a guide only. A physical check is to be made to ensure that all fluids are at the correct level.

| Ser | Assembly/System | Product | Capacity |
| --- | --- | --- | --- |
|  |  | Above –15 C | Below – 15 C | Litres | Pints |
| (1) | (2) | (3) | (4) | (5) | (6) |
| 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 | Engine (including filter) Gearbox Transfer Box Front and Rear Differentials Swivel pin housings Steering Box Steering Relay Winch drive, gearbox Propellor shafts General greasing General Lubrication Protective grease Clutch/brake fluid Windscreen washer Coolant (including heater) Fuel tank | OMD 80 OMD 80 OMD 80 OEP 220 OEP 220 OEP 220 OEP 220 OMD 80 XG 271 XG 279 OMD 80 PX 7 OX 8 AL 11/Water AL 39/Water Civgas | OMD 30 OMD 30 OMD 30 OEP 38 OEP 38 OEP 38 OEP 38 OMD 30 XG 271 XG 279 OMD 30 PX 7 OX 8 AL 11/Water AL 39/Water Civgas | 7.0 2.7 3.0 2.5 0.8 0.5 - 0.2 14.2 109 | 12.5 4.7 5.5 4.5 1.3 0.9 - 0.4 25 24 gals |

TABLE 3 – EQUIPMENT DATA

| Ser | Item | Detail |
| --- | --- | --- |
| (1) | (2) | (3) |
| 1 2 3 | TYRES: Size: Pressure: Front: Rear: ADJUSTMENTS: Fan belt deflection Compressor belt deflection TORQUE SETTINGS: Cylinder head bolts Rocker shaft bolts Inlet manifold bolts Exhaust manifold bolts Wheel nuts | 9.00 x 16 Tubed Road Cross-Country 2 bar (28 lb/sq.in.) 1.5 bar (21 lb/sq.in.) 2.4 bar (35 lb/sq.in.) 1.5 bar (21 lb/sp.in.) 14 mm (0.5”) midway between alternator and crankshaft pulleys. 14 mm (0.5”) midway between compressor and crankshaft pulleys 97 Nm (71.5 lbf ft) 40 Nm (29.5 lbf ft) 40 Nm (29.5 lbf ft) 20 Nm (15 lbf ft) 115 Nm (85 lbf ft) |

TABLE 4 – DRIVER/OPERATOR MAINTENANCE

Note….

The operations listed in this table are in addition to those detailed in JSP 351 “MT Drivers’ Handbook”.

| Ser | Task | Daily | Weekly | Monthly |
| --- | --- | --- | --- | --- |
|  |  | Before Use | After Use |  |  |
| (1) | (2) | (3) | (4) | (5) | (6) |
| 1. 2. 3. 4. 5. 6. 7. 8. 9. 10. 11. | Check: Correct functioning of all warning lights and gauges. For any fuel, oil or coolant leaks. Wheel hubs and brake drums for overheating. Refrigerant level indication in sight glass. Note: After running for 1 hour (Vehicles with air cooling system in operation only) During halts, after approx four hours running. See Cautions No. 1. Check/Top Up: Clutch/brake fluid reservoir Other Operations: Drain air reservoir (if applicable) Ambulances fitted with resuscitator (after use) Close down resuscitator Carry out pressure and flow test. Note: Procedures are detailed in Users Handbook Army Code 24044. Eberspacher B4L Heater (during warm weather when not in use). Switch on and operate briefly. Operate as detailed in User Handbook Army Code No. 24044. See Warning No. 5. | x x x | x x x x x x | x | x |

TABLE 5 – PERIODIC MAINTENANCE

| Ser | Task | Dia Ref | 800 mile/ initial | 3000 mile/3 monthly | 6000 mile/12 monthly | 24,000 mile/24 monthly |
| --- | --- | --- | --- | --- | --- | --- |
| (1) | (2) | (3) | (4) | (5) | (6) | (7) |
| 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 17 18 19 20 21 | Change oil in: Engine: See Caution No. 2 Note: The fuel pump electrical circuit is routed through the oil pressure switch. If the engine fails to start/run, prime oil pump in accordance with EMER Whld Veh 052. Gearbox Transfer Box Front and rear axle differentials Swivel pin housings Winch drive gearbox (if fitted) Check/Top Up: Swivel pin housings Steering box Winch drive gearbox (if applicable) Carburettor hydraulic dampers Steering relay Gearbox Transfer box Front and rear axle differentials Grease gun lubricate: Propeller shaft universal joints | x 6a,6c 11 2,3,4, 12,13, 14 | x x x x x x x x x | x x x | x x x x x x x x x x | x x x x x x x x x x |

(continued)

TABLE 5 – (Contd)

| Ser | Task | Dia Ref | 800 mile/ initial | 3000 mile/3 monthly | 6000 mile/12 monthly | 24,000 mile/24 monthly |
| --- | --- | --- | --- | --- | --- | --- |
| (1) | (2) | (3) | (4) | (5) | (6) | (7) |
| 22 23 24 25 26 27 28 29 30 31 32 | Grease gun lubricate: contd: Winch drive shaft universal joint (if applicable) Front and rear tow hooks Stretcher elevation gear (Qty 6 nipples) Note: One pump with a hand-powered grease gun to each nipple is sufficient. See Warning No. 6 Propeller shaft splines Procedure: Remove blanking plug fitted to splined end of propeller shaft. Fit grease nipple in place of blanking plug. Lubricate – five pumps of a hand powered grease gun is sufficient. Refit blanking plug. Note: If XG 271 is not immediately available, XG 279 may be temporarily substituted. Oil-can lubricate Accelerator, brake and clutch control linkages and clevis pins. All other clevis pins, catches seat mechanisms and similar fittings which require oiling but have no lubricators. Winch drive chain (if applicable) Winch drive shaft splines (if applicable) Winch guide rollers and sheaves (if appl.) | 10,15 6b 5 1,7,8,9 | x x x x x x x x | x x x x x x x | x x x x x x x x x | x x x x x x x x |

TABLE 5 – (Contd)

| Ser | Task | Dia Ref | 800 mile/ initial | 3000 mile/3 monthly | 6000 mile/12 monthly | 24,000 mile/24 monthly |
| --- | --- | --- | --- | --- | --- | --- |
| (1) | (2) | (3) | (4) | (5) | (6) | (7) |
| 33 34 35 36 37 38 39 40 41 42 43 44 45 46 47 48 49 | Oil-can lubricate: (contd): Winch cable (if applicable) Procedure: Fully extend and lubricate with an oil-soaked rag. Rewind cable under light tension Roof flaps and escape hatch mechanism (if applicable) Stretcher elevation drive chains. See Warning No. 6 Stretcher clamp pivot bolts. See Warning No. 6 Distributor mechansim Renew: Engine oil filter. See Cautions No. 2 Fuel filter element. Air cleaner element Engine breather filter Note: Fit new filter with the end marked IN facing upwards. Alternatively if the filter is marked with arrows they must point downwards. Engine flame traps. (Situated between each top rocker cover and air cleaner elbows) Torque tighten: Cylinder head bolts Rocker shaft bolts Inlet manifold bolts Exhaust manifold bolts Road wheel nuts |  | x x x x x x x x x x | x x x x x | x x x x x x x x | x x x x x x x x x x |

(continued)

TABLE 5 – (Contd)

| Ser | Task | Dia Ref | 800 mile/ initial | 3000 mile/3 monthly | 6000 mile/12 monthly | 24,000 mile/24 monthly |
| --- | --- | --- | --- | --- | --- | --- |
| (1) | (2) | (3) | (4) | (5) | (6) | (7) |
| 50 51 52 53 54 55 56 57 58 59 60 61 62 | Torque tighten: (contd): Other operations: Clean fuel sedimentor bowl and gauze filter. Resuscitation equipment only: Carry out pressure and flow tests as detailed in User Handbook AC 24044. See Cautions No.1. Air Cooling System only: Operate the system and check refrigerant level in sight glass. See Cautions No.1. Clean battery terminals and smear with grease. Remove and clean gauze and filters in ventilation system. Procedure: Wash with warm soapy water, rinse, dry and refit. Remove foreign matter from tubes, fins and intake grille of air cooling evaporator. Clean foam filter element. Clear exhaust pipe and combustion pipe of Eberspacher B4L heater. Note: An excessive carbon deposit in the exhaust denotes faulty heater system. Clean air cleaner element. Procedure: See Serial 56. Note: The element can be cleaned in this manner up to ten times. Clean glow/spark plug Eberspacher B4L heater. Note: Use non-ferrous metallic brush. |  | x x x | x x x x x x x | x x x x x x x x x x | x x x x x x x x x x |

(continued)

TABLE 5 – (Contd)

| Ser | Task | Dia Ref | 800 mile/ initial | 3000 mile/3 monthly | 6000 mile/12 monthly | 24,000 mile/24 monthly |
| --- | --- | --- | --- | --- | --- | --- |
| (1) | (2) | (3) | (4) | (5) | (6) | (7) |
| 63 64 | Other operations: (contd): Clean heater in-line filter. Note: This is a replaceable type filter and does not have a renewable element. Refit in accordance with fuel flow direction arrow. Remove, dismantle and check heat exchanger for corrosion or perforation. Eberspacher B4L heater. Note: This operation is to be carried out whether or not internal cleaning is required. |  |  |  | x | x x |

### TABLE 6 – OUT OF USE MAINTENANCE

Notes…

- This maintenance is to be carried out when the equipment is taken out of use for periods exceeding one month.

- An item of equipment taken out of use for periods exceeding four months is to be put into preservation in accordance with EMER Wheeled Vehicles A 019 Miscellaneous Instruction No.9.

- The equipment is to be cleaned, dried and stored under cover where possible.

- Any overdue maintenance is to be carried out when the equipment is brought back into use.

| Ser | Operation |
| --- | --- |
| (1) | (2) |
| 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 16 | Carry out Table 4 Maintenance and patch-paint Carry out next maintenance due Rectify all faults affecting roadworthiness Fill fuel tank Disconnect battery earth lead WEEKLY Check and adjust tyre pressures Report any fuel, oil or coolant leaks TWO MONTHLY Carry out Table 4 maintenance Operate equipment, ensuring operating temperature is reached and all oils are circulated Move equipment for a minimum of 8 km (5 miles) if circumstances permit Rectify all faults affecting roadworthiness Disconnect battery earth lead |

FIG 1

Fig 1 – Lubricating diagram