# Warco 918 Switch wiring

Right side of switch is main power in.

Pole 1 is looped to Pole 13

Pole 13 is looped to Pole 15

Pole 15 is looped to Pole 3

Pole 5    is looped to Pole 11

Pole 5 is also looped to pole 7 and brown mains wire

Pole 15 also looped to Pole 3 and blue mains wire

Pole 7 is looped to Pole 9.

Left side of switch is switched power to single phase motor. (original)

Pole 2 looped to Pole 10 and white to motor

Pole 6 is looped to Pole 8 and brown to motor

Pole 10 is looped to Pole 4 and black to motor

Pole 14 is looped to Pole 16 and blue to motor.

Blue also looped to capacitor.