IC703 HANDY REFERENCE (BOLD = Press for 1 second)

Tuning Steps- 		TS () TS DIAL TS

RECEIVE FUNCTIONS

Noise Blanker – 	DISPLAY (M) MENU (M3) F2

Filter - 		DISPLAY (M) MENU (M3) F1

AGC - 		DISPLAY (M) MENU (M4) F3

Noise Reduction - 	DISPLAY (S) MENU (S4) NR (F3 M-CH to set level)

Auto Notch Filter - 	DISPLAY (S) MENU (S4) F1

Split frequency operation - 	Tune receiver to DX station.

DISPLAY (M) MENU (M1) F2

F1 F3+DIAL

CW TX OPERATION

Select CW mode – 		MODE

Select key type – 		DISPLAY (M) MENU (M4) F2 MENU (K4) DIAL DISPLAY

Select CW R mode – 	DISPLAY (Q) MENU (Q3) DIAL DISPLAY

Adjust keying speed – 	DISPLAY (Q) MENU (Q2) DIAL DISPLAY

Adjust power – 		DISPLAY (Q) MENU (Q1) DIAL DISPLAY

Memory keyer functions

Send message memory – 		MODE F1/F3

Contest exchange – 		F2. MENU to decrease serial number by 1

Beacon mode send - 		MODE F1/F3

To edit keyer memory – 	MODE DISPLAY F1 F1/F2/F3

F1 OR F3 to arrow back/forward. Rotate DIAL for character

^ before a word deletes spaces between characters ie AR

* is used to insert contest number

F2 to delete spaces. MENU MENU MENU

Set contest number - 	MODE DISPLAY F2

SSB TX OPERATION

Select SSB mode – 	MODE (then MODE for alternative sideband)

Adjust mic gain – 		DISPLAY (Q) MENU (Q2) DIAL (note ALC meter) DISPLAY

Adjust power – 		DISPLAY (Q) MENU (Q1) DIAL DISPLAY

Speech Compressor - 	DISPLAY (M) MENU (M4) F2

VOX - 			DISPLAY (M) MENU (M4) F1

Metering - 			DISPLAY (M) MENU (M3) F3

DIGITAL MODES OPERATION

Select USB Digital mode -	MODE to select RTTY. MODE to select Digital (flashing USB)

Select LSB Digital mode – In USB digital mode, DISPLAY MENU (Q2) DIAL (L)

(Connect interface to DATA socket. For TX unplug speakers from PC)

MEMORY CHANNEL OPERATION (105 memory channels/6 scan edge channels)

Read memory channel – 	DISPLAY (M) MENU (M2) F3

Rotate M-CH to select memory channel

F3 to revert to VFO mode

Write memory/scan edge ch -	Set desired frequency/mode etc

DISPLAY (M) MENU (M2)

Rotate M-CH to select memory channel/scan edge ch F1

Name memory channel -		Call up memory DISPLAY (M) MENU (M2) F3 M-CH

DISPLAY (G) MENU (G4) F3

F1 OR F3 to arrow back/forward.

Rotate DIAL for character. F2 to delete spaces. DISPLAY

Display memory names - 	DISPLAY (G) MENU (G4)

Erase memory -			DISPLAY (M) MENU (M2) F3

Rotate M-CH to select memory channel F2

F3 to revert to VFO mode

Programmed scan -	 	In VFO mode DISPLAY (S) MENU (S2) F1

Memory scan - 			In memory mode DISPLAY (S) MENU (S2) F1

Select memory scan - 		In memory mode DISPLAY (S) MENU (S2)

M-CH to select memory channels. F2 to include. F1 F2

F2 to deselect all memory channels

Priority Watch - 			Call up (or write new) memory channel to watch

Close squelch if desired. DISPLAY (S) MENU (S2) F3 F2

F2 to cancel

Write memo pads (max 10) - 	DISPLAY (S) MENU (S1) F2

Read memo pads -		DISPLAY (S) MENU (S1) F3