IC-703 info

Phil Salas – AD5X

IC-703 power vs current vs display measurements.  All backlighting/keylighting turned off (most efficient mode).  All measurements made on 40 meters.  Power measured with Diamond SX-1000 power meter.  The “Display Est.” is my best determination of power by trying to read the Po bargraph display.

|  |  | +13.8VDC |  |  |  | +9.6VDC |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| TX# | Pout | Display Est. | Current |  | Pout | Display Est. | Current |
| H | 10W | 10W | 1.9A |  | 5W | 5W | 1.5A |
| 9 | 8.5W | 9W | 1.8A |  | 4.25W | 4.5W | 1.4A |
| 8 | 6.5W | 7W | 1.7A |  | 3.5W | 3.5W | 1.3A |
| 7 | 5W | 5W | 1.5A |  | 2.8W | 3W | 1.3A |
| 6 | 4W | 4W | 1.4A |  | 2.25W | 3W | 1.2A |
| 5 | 3W | 3W | 1.3A |  | 1.8W | 2.5W | 1.1A |
| 4 | 2W | 2.5W | 1.2A |  | 1.25W | 2W | 1.0A |
| 3 | 1.5W | 2W | 1.1A |  | 0.8W | 1.5W | 1.0A |
| 2 | 0.8W | 1.5W | 1.0A |  | 0.5W | 1W | 0.9A |
| 1 | 0.5W | 1W | 0.9A |  | 0.25W | 1W | 0.8A |
| L | 0.1W | <1W | 0.8A |  | 0.1W | <1W | 0.8A |

I’ve also determined that my IC-703 puts out full power (10 watts) into a 2:1 VSWR.  At a 3:1 VSWR, power folds back to about 3-4 watts.  I didn’t check power at other VSWR settings.