UNIVERSAL PROGRAMMER & TESTER POWER-100/EXPRO-60/80

README.DOC
**********

1. POWER-100 or EXPRO-60/80 has consolidated its with coloured pull-down menu
   driver software into 2 diskettes,
   Diskette POWER-100 or EXPRO-60/80 #1 consists of the following files:

     DEVICE.LST  : POWER-100 or EXPRO-60/80 can program Device's list.
     INSTALL.BAT : Installation batch file.
     EXPROXXX.EXE: EXPRO-60/80 executable SELF-EXTRACTING file includes
                   main program, edit-driver ,disassembler files and utility
                   files.
     POWERXXX.EXE: POWER-100 executable SELF-EXTRACTING file includes
                   main program, edit-driver ,disassembler files and utility
                   files.
     README.DOC  : This document records the information of revision of
                   S/W and H/W.

   Diskette POWER-100 or EXPRO-60/80 #2 consists of the following files:

     EXPRODRV.EXE: EXPRO-60/80 executable SELF-EXTRACTING file includes
                   all device driver files.

     POWERDRV.EXE: POWER-100 executable SELF-EXTRACTING file includes
                   all device driver files.

Note: EXPRO-60/80 software was released on Sept 1992, all EXPRO-60
      software before this date is not compatible with present
      software. Please do not mix them up.

2. To enhance EXPRO-60/80's software function and make it easier to
   operate, great amendments were made on the software driver. In
   addition to altering into coloured version, other changes are:

   a) pull-down menu driver furnishes user with simple operating
      environment
   b) detailed status field display provides user with complete IC
      programming information, work path and current working file
   c) all functions can be operated under main-menu providing user
      with continuous operating procedures
   d) equipped with user definable Macrofile function and QUICKLY keys
      which greatly simplifies user's operating procedures

3. INSTALLATION

   This segment describes the method of installing an UNIVERSAL
   programmer on an IBM PC/XT/AT/386/486 computer or compatible
   running MS-DOS or PC-DOS.
   It is assumed that the installer is familiar with the installation
   of PC add-on cards and software in PCs running MS-DOS.

   3.1 Host System Requirements

     *IBM PC/XT/AT/386/486 or compatible PC.
     *PC/386DX-33 or faster is recommended.
     *Min. 640K bytes memory.
     *Min. One floppy disk drive. A hard disk is preferable.
     *Operation system :MS-DOS or PC-DOS ,version 3.3 or later.

   3.2 Software Installation Procedures
     Running the INSTALL.BAT to setup POWER-100's or EXPRO-60/80's S/W to
     HARD disk.

     Running POWER.EXE(for POWER-100) or EXPRO.EXE(for EXPRO-60/80) will
     start the system when installation is completed.

4. About GANGs Adaptors using

    ADP-GAL16V18,   ADP-GAL20V8,    ADP-CE16V8, ADP-CE20V8,  ADP-N3001,
    ADP-PEEL18CV8,  ADP-PEEL22CV10, ADP-EP32,   ADP-EP40,    ADP-EP32A-PLCC,
    ADP-EP32B-PLCC, ADP-EP40-PLCC,  ADP-51F,    ADP-48F.

   The adaptors listed above are GANGs adaptors (can program 4 devices
   simultaneously). These GANGs adaptors' driver program (all in Adaptor
   #3 diskette) needs to be independently executed and cannot be called
   through "POWER.EXE" or "EXPRO.EXE". Therefore, the GANGs adaptor driver
   file does not need to be in the same directory as POWER.EXE or EXPRO.EXE
   while non-GANGs adaptor driver file must be in the same directory as
   POWER-100 or EXPRO.EXE to be conveniently called through POWER.EXE or
   EXPRO.EXE.

 5. Revision of EXPRO.EXE or POWER-100

   Version V7.00: On Sept 1, 1992, EXPRO-80 hardware and software were
                  formally released. Software is compatible with
                  EXPRO-60 hardware and will automatically identify
                  between EXPRO-60 and EXPRO-80 hardware.

                  Due to the restriction of DOS, our software can only
                  allocate memory buffer to the maximum of 256K bytes
                  (2 Mbits), thus we have in the "RunFunc" menu,
                  "Copy file to EPROM" and "Read EPROM to file" these
                  two functions to solve the problem of insufficient
                  memory buffer.
                  Below is its operating procedure:
                  "Read EPROM to file" - Software will require you to
                    input filename, then display "Ready to Read (Y/<CR>)?".
                    If you press 'Y', software will read EPROM's content on
                    the textool and save it into diskette.

                  "Copy file to EPROM" - Software will require you to select
                    the file to be copied to the EPROM file. After selection,
                    software will inquire "Ready to program (Y/<CR>)?".
                    When 'Y' is pressed, software will read the file's
                    content and program it to EPROM.

   Version V7.10: On Nov 1,1992, software was updated with function of
                  executing adaptor with driver program. If you happen
                  to wish to program a Device that requires an adaptor,
                  the right bottom corner of Status field will display
                  "ADAPTOR: adaptor's module name" to remind you the
                  need of an adaptor in order to program.

   Version V7.13: On Nov 20, 1992, to simplify user's operating procedure,
                  "Macro setup" and "Run Macro" were included in Misc.'s menu.

                  Briefly, MACRO's function in 'Misc.' are (1) Macro setup
                  (2) Run Macro,
                  Step 1: After selecting "Macro setup", the bottom corner
                          of status field displays " [Macro Mode]:<F9> to
                          abort, <F10> to save". Every operating procedure
                          will be recorded by the software till you press
                          <F10>. Software will then require you to input
                          Macro filename, after entering the filename,
                          "[Macro Mode]:..." will then vanish.

                  Step 2: After selecting "Run Macro", software will
                          require you to input the Macro file to be
                          executed. "Macro processing" will appear on
                          the bottom corner of status field after selecting
                          Macro file till execution is completed.

   Version V7.15: On Dec 17, 1992, for the convenience of user, software
                  was updated to classify IC Test into the following:
                  1. Logic IC test     : Test TTL74 , CMOS40/45 series
                  2. Dynamic RAM test  : Test Dynamic RAM
                  3. Static RAM test   : Test Static RAM
                  4. User vector editor: User can edit Vector and test
                                         ICs that we did not include in
                                         our Type. Modes selectable are
                                         8, 14, 16, 20, 24, 28, 32 and 40
                                         pins.

   Version V7.22: On Mar 23, 1993, EXPRO /M=MACROfilename
                  If you want to run MACRO file after entering
                  EXPRO.EXE program, you could input "EXPRO /M=MARCOFILENAME"
                  at DOS prompt.

   version V8.00 : May 31, 1993

     EXPRO.EXE V8.00 has the following modifications:

     a. Software V8.00 can be used with either SAC-101A, System Adaptor Card or
        LINK-P1, Printer Port Adaptor Module to control EXPRO-60/80 hardware.
        The software automatically detects the kind of interface used. To
        avoid confusions with old versions, the programming driver files' file
        extention name EXE has been changed to BIN.

     b. V8.00 and later versions simplify Read/Program of high-capacity EPROM.
        When user selects EPROM size larger than software allocated memory
        buffer, software opens a file (EDBIN.MEM) with same EPROM size
        automatically in the "Work path" to use file buffer when software
        access EPROM's data.

        Example:

        Assumption: software allocated memory buffer space is 256K bytes
        Work path: D:\EXPRO\

        When programming 27C040 (512 Kbytes), allocated memory buffer becomes
        insufficient. Software automatically opens a 512 Kbytes file
        (D:\EXPRO\EDBIN.MEM). If file opening is successful, "EDBIN.MEM" will
        appear after "Buffer address :" inside the status field. After this,
        the user may change work path's directory and not affect EDBIN.MEM
        access.

        Upon exiting the main program, D:\EXPRO\EDBIN.MEM is recorded in
        EXPRO.DAT for future use. As not to occupy disk space,
        D:\EXPRO\EDBIN.MEM is deleted.

   NOTE: For executing the above, take note of the following:

       a. If the PC's memory RAM is sufficient, it is suggested that the
          excess memory RAM be set into RAM DISK (refer to DOS manual).
          This way, the maximum speed can be attained during Read/Program
          EPROM and avoid hard disk Read/Write frequency.

       b. If the PC has insufficient RAM, it is suggested that the biggest free
          space of hard disk of faster access time be used as not to affect the
          speed of Read/Program EPROM.

       c. If the disk space is insufficient or Read/Write is not possible,
          "Disk-Buffer access error. Refer to README.DOC" would appear on the
          screen. At this point, determine if there is sufficient buffer to
          access EPROM data based on the length of the "Buf start:","Buf end:"
          and "Dev start:","Dev end:" inside  the status field. If buffer is
          insufficient, solve the above problem on the disk before reentering
          main program.

   version V8.20 : May 15, 1994

     POWER.EXE or EXPRO.EXE V8.20 has the following modifications:

     Configuration Menu:

     A. Memory Initialization: Initial the content of memory and disk-buffer.

        "00H","FFH" can be toggled by pressing [ENTER] key.  After entering
      Main program (POWER.EXE OR EXPRO.EXE), the set value will be used to
      initialize the content of memory and disk-buffer.

     B. Disk-Buffer Path: Set up disk number and path of the disk-buffer.

        When the DOS allocated memory buffer is out of space, system will
      automatically use the set value to create additional disk-buffer.
      Fast speed RAM-Disk or Hard disk is recommended.

     C. Self-testing [ON/OFF]: Self testing function [ENABLE/DISABLE].

        When enabled, system will perform self-testing function on all
      programming driver circuit before entering Main-menu.  When there is
      hardware circuit error, system will warn the user with error messages
      and run "SELFDIAG.EXE" to perform further testing and diagnosis.  This
      procedure should only take 4-10 seconds, we highly recommend this
      self-testing procedure. (For POWER-100 only)

      [ON/OFF] can be toggled by pressing [ENTER] key.

     D. IC inserted test [ON/OFF]: Test IC inserted position [ENABLE/DISABLE].

        When enabled, system performs IC inserted position test before
      programming the IC. This test is to prevent any damage to the IC
      inserted.   Furthermore, to protect the hardware of the programmer
      from being damaged by overcurrent, system warns the user with
      "IC overcurrent" message when this situation occurs and discontinues
      the IC programming process.(For POWER-100 only)

      [ON/OFF] can be toggled by pressing [ENTER] key.

     E. Auto sense [ON/OFF]:  Auto sensing function [ENABLE/DISABLE].

        When enabled, after entering any "Runfunc-menu" function, system
      automatically senses the socket of the programmer to check if there
      is any IC placed in it.  If IC is placed, system automatically enter
      "Runfunc" without the need of pressing "YES" key.  This function will
      simplify and benefit large volume production.(For POWER-100 only)

      Note: when this function is enabled, after entering any "Runfunc-menu"
            function, the "BUSY" LED of the POWER-100 will be turned on.

      [ON/OFF] can be toggled by pressing [ENTER] key.

<<< IMPORTANT AMEND !!! >>>

   version V8.25 : April 30, 1994

     The following mention is for POWER-100 only.

                        POWER-100 HARDWARE REVISION

        Due to the drivers of different PC's printer port, We were forced
     to make some  changes to the hardware of the POWER-100, We feel sorry
     to ask you to also do the necessary changes  to your  POWER-100 system.
     For those  of you who are using software version V8.20 and prior
     version,   the following  procedures is necessary,

     1. Open POWER-100 and take out U21 (Lattice GAL16V8 or AMD PALCE16V8)
        from bottom board( PCB NO. : EXPRO-100 PCB-E0007 ).
     2. Use the JEDEC file provided under "UTIL" directory--"POWER.JED"
        to program to the U21.
     3. After the programming step is completed ok, put the U21 back.
     4. Make sure all the steps stated above is correctly done, continue
        to use version V8.25 or later software.

   version V8.25 : April 30, 1994

     The following mention is for EXPRO-60/80 only.

                        LINK-P1 HARDWARE REVISION

        Due to the drivers of different PC's printer port, We were forced
     to make some  changes to the hardware of the LINK-P1, We feel sorry
     to ask you to also do the necessary changes  to your  LINK-P1 system.
     For those  of you who are using software version V8.20 and prior
     version,   the following  procedures is necessary,

     1. Open LINK-P1 and take out U2 (Lattice GAL16V8 or AMD PALCE16V8).
     2. Use the JEDEC file provided under "UTIL" directory--"LINK-P1.JED"
        to program to the U2.
     3. After the programming step is completed ok, put the U2 back.
     4. Make sure all the steps stated above is correctly done, continue
        to use version V8.25 or later software.

6.New additional DEVICEs list

  ALTERA:
                EPC1064/V( for POWER-100 & EXPRO-80 only )
                EPC1213  ( for POWER-100 & EXPRO-80 only )
                #EPM7064LC44 ( for POWER-100 )                  DATE:04/07/94
                *EPM7064LC68 ( for POWER-100 & EXPRO-80 only )  DATE:04/07/94
                *EPM7064LC84 ( for POWER-100 & EXPRO-80 only )  DATE:04/07/94
  AMD :
                Am28F010A,Am28F020A,MACH120,MACH220
                MACH130,MACH230                         DATE:16/9/94
  ATMEL:
                AT29C512,AT27C4096
                AT89C52                                 DATE:21/10/94
                ATF16V8B/L,ATF20V8B/L                   DATE:01/13/95
                ATF22V10B/L                             DATE:02/21/95
                AT89C1051,AT89C2051                     DATE:01/18/95
                ATV750B/BL                              DATE:02/22/95
  CATALYST:
                CAT28C16V3
  CYPRESS:
                CY7C291A,CY7C292A,CY7C256
                CY27H010                                DATE:07/10/94
                PALCE16V8                               DATE:02/21/95
  DALLAS:
                DS1220AB/AD,DS1225AB/AD,DS1225D/DE,DS1225Y
                DS1230Y/AB, DS1245Y/AB
                DS87C520                                DATE:01/13/95
  FUJITSU:
                28F010                                  DATE:7/10/94
                MBM27C4096                              DATE:21/10/94
  HITACHI:
                HN27C4000G                              DATE:12/29/94
  ICT:
                PA7140                                  DATE:02/21/95
  INTEL:
                8795BH,8798 ( for POWER-100 only )
       NOTICE: The above ICs must be inserted backward in the textool.
               ÕÍÍÍÍÍÍÍÍÍ¸                         ÕÍÍÍÍVÍÍÍÍ¸
        PIN-25Ä¶ ÍÍ   ÍÍ ÇÄPIN-24            PIN-1Ä¶ ÍÍ   ÍÍ ÇÄPIN-48
        PIN-26Ä¶ ÍÍ   ÍÍ ÇÄPIN-23            PIN-2Ä¶ ÍÍ   ÍÍ ÇÄPIN-47
        PIN-27Ä¶ ÍÍ   ÍÍ ÇÄPIN-22            PIN-3Ä¶ ÍÍ   ÍÍ ÇÄPIN-46
            .  º 8795BH  º    .                  . º         º .
            .  º   or    º    .                  . º 48-PINS º .
            .  º  8798   º    .  Backward insert . º TEXTOOL º .
            .  º         º    .  ==============> . º         º .
               º         º                         º         º
        PIN-46Ä¶ ÍÍ   ÍÍ ÇÄPIN-3            PIN-22Ä¶ ÍÍ   ÍÍ ÇÄPIN-27
        PIN-47Ä¶ ÍÍ   ÍÍ ÇÄPIN-2            PIN-23Ä¶ ÍÍ   ÍÍ ÇÄPIN-26
        PIN-48Ä¶ ÍÍ   ÍÍ ÇÄPIN-1            PIN-24Ä¶ ÍÍ   ÍÍ ÇÄPIN-25
               ÔÍÍÍÍ^ÍÍÍÍ¾                         ÔÍÍÍÍÍÍÍÍÍ¾

  ISSI:
                IS93C46-3,IS93C56-3,IS28F010            DATE:11/24/94

  LATTICE:
                GAL6001B,GAL6002B                       DATE:02/23/95
  MICROCHIP:
                PIC16C84,PIC16C64(for POWER-100 only),PIC16C58
  MITSUBISHI:
                M5M28C64A
  MIXC:
                MX27L1000,MX27C1001,MX27C4100,MX27C4096
                MX27L256,MX27L512,MX27L4000,MX27C4111   DATE:21/10/94
  MOTOROLA:
                MC68HC711D3-PLCC(for POWER-100 only)    DATE:11/09/94
  NEC:
                uPD28C64
                uPD75P108B                              DATE:12/30/94
  OKI:
                MSM28C16A
  PHILIPS:
                87C504, 87C524,87C575,87C51FC           DATE:01/18/95
  SII:
                S-2840A,S-2812A/17A,S-2860A/64A
  WINBOND:
                W27F010,W29EE011,W27F512,W27E512,W27E010 DATE:04/07/95
  SGS-THOMSON:
                ST62E10/T10,ST62E20/T20,ST62E15/T15,ST62E25/T25
       NOTICE:  The above ICs must be inserted backward in textool.
                It mean IC's pin-1 is mapped to textool's pin-22
                (at EXPRO-80) or pin-21 (at EXPRO-60).(POWER-100 no need)
                M27C160                                 DATE:7/10/94
                M27C801,M28C64C                         DATE:21/10/94
  XILINX:
               XC1736D,XC1765D,XC17128,XC17128D,XC17256D
       NOTICE: You have to connect a resistor(1.5K ohm) between PIN2 and PIN8
               of IC when you use EXPRO-60 H/W. Because the speed of
               EXPRO-60's driver pins are too slow.

7. To program EPROM by way of EVEN/ODD ( with driver file EPP1024.BIN
   version V7.05 for 1M to 8M or driver file EPP512.BIN version V7.02
   for 2716 to 27512 ), you can operate as follows,

   EX: PROGRAM 27C256
       a. Modify zone
          Buffer start : 0
          Buffer end   : 3FFF
          Device start : 0

    When you press 'Even' in the program function, software will execute
    program procedure and halt at EPROM address 3FFF.

       b. Modify zone
          Buffer start : 0
          Buffer end   : 7FFF
          Device start : 4000

    When you press 'Odd' in the program function, software will execute
    program procedure and halt at address 7FFF.


8. The function of the "PLD Vector Test" is to test the internal circuit
   of the PLD.

   Test procedures:
      a. Vector Table must be built when designing the PLD equation.
         (Refer to the usage of PLD Assemblers)
      b. After Assembler, the Vector Table is included in the Jedec
         file generated by the Assembler.
      c. After using the programmer to program the PLD successfully,
         perform the " PLD Vector Test".
      d. Select correct Type by "T. Select Type" Sub-menu.
      e. After entering function" L. Load Test Vector of JEDEC file"
         download the JEDEC file to memory buffer.
      f. Then, enter function "F. Function Test", or "O. Loop Test",
         to test the internal Circuit of the PLD.

Note: "V. View Vector" function can be used to view the Vector downloaded.
      "S. Set Vcc" function can be used to set the Voltage Vcc value for
      testing the PLD.

9. if POWER-100 communicates error with PC's printer port, refer to following:

   a. Before using POWER-100, please check the AC voltage (110 or 220 ACV)
      switch which is located at base of the unit.
   b. POWER-100 should not be connected to SAC-101A. If it happens, the
      unit's bottom board's U21(GAL-16V8) will be damaged. If so, please
      replace it with another GAL16V8. In the POWER-100 "Util" path,
      there is power.jed which is fuse map of U21.
   c. If the above steps are correct, then connect the POWER-100 to the PC's
      printer port, turn on the power, execute power.exe, then the s/w will
      search for the POWER-100 via the PC's printer port to see which I/O
      port it has been installed and there's no need for the user to make the
      seting.
   d. If the problem still exists after the above steps, then disconnect the
      POWER-100 from the printer port and test the printer port with a printer
      to check if the printer can print. If it can't print, then the super
      I/O card should faultily. If it prints, then it might be caused by the
      interference coming from the super I/O card since some cards produce
      interferences, therefore use another super I/O card to test and let us
      know its brand for our information.
   e. Please send us the POWER-100 for repair, if still it can't work.


  --------------------------------------------------------------------
   UPDATE INFORMATION FOR SOFTWARE VERSION 8.41
  --------------------------------------------------------------------


   DRIVER FILE       OLD V.    NEW V.         ADD ITEM
   -------------------------------------------------------------------
   EEP3B              8.18     8.19        ADD ATMEL      AT29C020
                                               ATMEL      AT29LV020
                                               HITACHI    HN58064

   SEEP4              8.17     8.18        ADD MICROCHIP  24C32
                                                          24LC32
                                                          24LC65

   SEEP1              8.18     8.18                       24C08
                                                          24LC08

   GAL2               8.20     8.21        MODIFY FOR AMD PALCE20V8PLCC
                                           "IC OVER CURRENT" PROBLEM.