Serial Ports and Cables

| Serial connections are found on many common peripheral devices such as modems, printers, and mice. Serial connections are capable of only transmitting a single bit at a time, which keeps them designated to the lower bandwith devices. Much like parallel interfaces, serial ports had remained virtually unchanged since their inception. The original specification, RS-232, was finally upgraded to RS-422 and RS-423. |
| --- |
| DB25 Standard Serial Pinout: EIA-232-D (RS-232-D), ITU-TSS (CCITT) V.24/V.28, ISO 2110 |
| Male DB25 | Female DB25 |
| Pin | Signal Name | Abbreviation | RS-232 Circuit Ref. | V.24 Circuit Ref. | Signal Function/ Direction |
| 1 | Shield | SHD | AA | 101 | Ground |
| 2 | Transmitted Data | TD | BA | 103 | Data, to DCE |
| 3 | Received Data | RD | BB | 104 | Data, from DCE |
| 4 | Request to Send | RTS | CA | 105 | Control, to DCE |
| 5 | Clear to Send | CTS | CB | 106 | Control, from DCE |
| 6 | DCE Ready | DCR | CC | 107 | Control, from DCE |
| 7 | Signal Ground | SGND | AB | 102 | Ground |
| 8 | Received Line Signal Detector | RLSD | CF | 109 | Control, from DCE |
| 9 | +12 VDC Reserved for Testing |  |  |  |  |
| 10 | -12 VDC Reserved for Testing |  |  |  |  |
| 11 | Unassigned |  |  |  |  |
| 12 | Secondary Received Line Signal Detector | SRLSD | SCF | 122 | Control, from DCE |
| or |
| 12 | Data Signal Rate Selector | DSRSC | CI | 112 | Control, from DCE |
| 13 | Secondary Clear to Send | SCTS | SCB | 121 | Control, from DCE |
| 14 | Secondary Transmit Data | STD | SBA | 118 | Data, to DCE |
| 15 | Transmitter Signal Element Timing | TSETC | DB | 114 | Timing, from DCE |
| 16 | Secondary Receive Data | SRD | SBB | 119 | Data, from DCE |
| 17 | Receiver Signal Element Timing | RSETC | DD | 115 | Timing, from DCE |
| 18 | Local Loopback | LL | LL | 141 | Control, to DCE |
| 19 | Secondary Request to Send | SRTS | SCA | 120 | Control, to DCE |
| 20 | DTE Ready | DTR | CD | 108.2 | Control, to DCE |
| 21 | Remote Loopback | RL | RL | 140 | Control, to DCE |
| or |
| 21 | Signal Quality Detector | SQD | CG | 110 | Control, from DCE |
| 22 | Ring Indicator | RI | CE | 125 | Control, from DCE |
| 23 | Data Signal Rate Selector | DSRST | CH | 111 | Control, to DCE |
| or |
| 23 | Data Signal Rate Selector | DSRSC | CI | 112 | Control, from DCE |
| 24 | Transmitter Signal Element Timing | TSETT | DA | 113 | Timing, to DCE |
| 25 | Test Mode | TM | TM | 142 | Control, from DCE |

| DB9 Serial Pinout for IBM AT and compatible computers: EIA/TIA-574 |
| --- |
| Male DB9 | Female DB9 |
| Pin | Signal Name | Abbreviation | RS-232 Circuit Ref. | V.24 Circuit Ref. | Signal Function/ Direction |
| 1 | Received Line Signal Detector | RLSD | CF | 108 | Control, from DCE |
| 2 | Received Data | RD | BB | 104 | Data, from DCE |
| 3 | Transmitted Data | TD | BA | 103 | Data, to DCE |
| 4 | DTE Ready | DRT | CD | 108.2 | Control, to DCE |
| 5 | Signal Ground | SGND | AB | 102 | Ground |
| 6 | DCE Ready | DCR | CC | 107 | Control, from DCE |
| 7 | Request to Send | RTS | CA | 105 | Control, to DCE |
| 8 | Clear to Send | CTS | CB | 106 | Control, from DCE |
| 9 | Ring Indicator | RI | CE | 125 | Control, from DCE |

| RJ45 Serial Pinout: EIA/TIA-561 (ANSI/EIA-232-D) |
| --- |
| Male RJ-45 (Plug) | Female RJ-45 (Socket) |
| Pin | Signal Name | Abbreviation | RS-232 Circuit Ref. | V.24 Circuit Ref. | Signal Function/ Direction |
| 1 | DCE Ready | DCR | CC | 107 | Control, from DCE |
| or |
| 1 | Ring Indicator | RI | CE | 125 | Control, from DCE |
| 2 | Received Line Signal Detector | RLSD | CF | 109 | Control, from DCE |
| 3 | DTE Ready | DTR | CD | 108.2 | Control, to DCE |
| 4 | Signal Ground | SGND | AB | 102 | Ground |
| 5 | Received Data | RD | BB | 104 | Data, from DCE |
| 6 | Transmitted Data | TD | BA | 103 | Data, to DCE |
| 7 | Clear to Send | CTS | CB | 106 | Control, from DCE |
| 8 | Request to Send | RTS | CA | 105 | Control, to DCE |

| Apple Macintosh Serial |
| --- |
| Male MiniDin8 | Female MiniDin8 |
| Pin | Signal Name | Abbreviation | Signal Function/ Direction |
| 1 | Handshake Output (DTR) | HSKo, +12V | Control, to DCE |
| 2 | Handshake Input (DSR) | HSKG | Control, from DCE |
| 3 | Transmitted Data (Minus) | TXD- | Data, to DCE |
| 4 | Signal Ground | GND | Ground |
| 5 | Received Data (Minus) | RXD- | Data, from DCE |
| 6 | Transmitted Data (Plus) | TXD+ | Data, to DCE |
| 7 | Unassigned |  |  |
| 8 | Received Data (Plus) | RXD+ | Data, from DCE |

| DB37 Serial Pinout: EIA-449 (RS-449), ISO 4902 |
| --- |
| Male DB37 | Female DB37 |
| Pin | Signal Name | Mnem. | V.24 Circuit Ref. | Signal Function/ Direction |
| 1 | Shield | AA | 101 | Ground |
| 2 | Signal Rate Indicator | SI | 112 | Control, from DCE |
| 3 | Unassigned |  |  |  |
| 4 | Send Data A | SD A | 103 | Data, to DCE |
| 5 | Send Timing A | ST A | 114 | Timing, from DCE |
| 6 | Reveive Data A | RD A | 104 | Data, from DCE |
| 7 | Request to Send A | RS A | 105 | Control, to DCE |
| 8 | Reveive Timing A | RT A | 115 | Timing, from DCE |
| 9 | Clear to Send A | CS A | 106 | Control, from DCE |
| 10 | Local Loopback | LL | 141 | Control, to DCE |
| 11 | Data Mode A | DM A | 107 | Control, from DCE |
| 12 | Terminal Ready A | TR A | 108.2 | Control, to DCE |
| 13 | Reveiver Ready A | RR A | 109 | Control, from DCE |
| 14 | Remote Loopback | RL | 140 | Control, to DCE |
| 15 | Incoming Call | IC | 125 | Control, from DCE |
| 16 | Select Frequency | SF | 126 | Control, from DCE |
| 17 | Terminal Timing A | TT A | 113 | Timing, to DCE |
| 18 | Test Mode | TM | 142 | Control, from DCE |
| 19 | Signal Ground | SG | 102 | Ground |
| 20 | Reveive Common | RC | 102b | Ground |
| 21 | Unassigned |  |  |  |
| 22 | Send Data B | SD B | 103 | Data, to DCE |
| 23 | Send Timing B | ST B | 114 | Timing, from DCE |
| 24 | Receive Data B | RD B | 104 | Data, from DCE |
| 25 | Request to Send B | RS B | 105 | Control, to DCE |
| 26 | Receive Timing B | RT B | 115 | Timing, from DCE |
| 27 | Clear to Send B | CS B | 106 | Control, from DCE |
| 28 | Terminal in Service | IS | N/A | Control, to DCE |
| 29 | Data Mode B | DM B | 107 | Control, from DCE |
| 30 | Terminal Ready B | TR B | 108.2 | Control, to DCE |
| 31 | Reveiver Ready B | RR B | 109 | Control, from DCE |
| 32 | Select Standby | SS | 116 | Control, to DCE |
| 33 | Signal Quality | SQ | 110 | Control, from DCE |
| 34 | New Signal | NS | N/A | Control, to DCE |
| 35 | Terminal Timing B | TT B | 113 | Timing, to DCE |
| 36 | Standby Indicator | SB | 117 | Control, from DCE |
| 37 | Send Common | SC | 102a | Ground |

| DB9 Secondary Channel Pinout |
| --- |
| Male DB9 | Female DB9 |
| Pin | Signal Name | Mnem. | V.24 Circuit Ref. | Signal Function/ Direction |
| 1 | Shield | AA | 101 | Ground |
| 2 | Secondary Reveiver Ready | SRR | 122 | Control, from DCE |
| 3 | Secondary Send Data | SSD | 118 | Data, to DCE |
| 4 | Secondary Receive Data | SRD | 119 | Data, from DCE |
| 5 | Signal Ground | SG | 102 | Ground |
| 6 | Reveive Common | RC | 102b | Ground |
| 7 | Secondary Request to Send | SRS | 120 | Control, to DCE |
| 8 | Secondary Clear to Send | SCS | 121 | Control, from DCE |
| 9 | Send Common | SC | 102a | Ground |

| DB25 Serial Pinout: EIA-530 (RS-530) |
| --- |
| Male DB25 | Female DB25 |
| Pin | Signal Name | Abbreviation | RS-232 Circuit Ref. | V.24 Circuit Ref. | Signal Function/ Direction |
| 1 | Shield | SHD | AA | 101 | Ground |
| 2 | Transmitted Data A | TD A | BA | 103 | Data, to DCE |
| 3 | Received Data A | RD A | BB | 104 | Data, from DCE |
| 4 | Request to Send A | RTS A | CA | 105 | Control, to DCE |
| 5 | Clear to Send A | CTS A | CB | 106 | Control, from DCE |
| 6 | DCE Ready A | DCR A | CC | 107 | Control, from DCE |
| 7 | Signal Ground | SGND | AB | 102 | Ground |
| 8 | Received Line Signal Detector A | RLSD A | CF | 109 | Control, from DCE |
| 9 | Receiver Signal Element Timing (DCE Source) B | RSETC B | DD | 115 | Timing, from DCE |
| 10 | Received Line Signal Detector B | RLSD B | CF | 109 | Control, from DCE |
| 11 | Transmitter Signal Element Timing (DTE Source) B | TSETT B | DA | 113 | Timing, to DCE |
| 12 | Transmitter Signal Element Timing (DCE Source) B | TSETC B | DB | 114 | Timing, from DCE |
| 13 | Clear to Send B | CTS B | CB | 106 | Control, from DCE |
| 14 | Transmitted Data B | TD B | BA | 103 | Data, to DCE |
| 15 | Transmitter Signal Element Timing (DCE Source) A | TSETC A | DB | 114 | Timing, from DCE |
| 16 | Reveived Data B | RD B | BB | 104 | Data, from DCE |
| 17 | Receiver Signal Element Timing (DCE Source) A | RSETC A | DD | 115 | Timing, from DCE |
| 18 | Local Loopback | LL | LL | 141 | Control, to DCE |
| 19 | Request to Send B | RTS B | CA | 105 | Control, to DCE |
| 20 | DTE Ready A | DTR A | CD | 108.2 | Control, to DCE |
| 21 | Remote Loopback | RL | RL | 140 | Control, to DCE |
| 22 | DCE Ready B | DCR B | CC | 107 | Control, from DCE |
| 23 | DTE Ready B | DTR B | CD | 108.2 | Control, to DCE |
| 24 | Transmitter Signal Element Timing (DTE Source) A | TSETT A | DA | 113 | Timing, to DCE |
| 25 | Test Mode | TM | TM | 142 | Control, from DCE |

| M/34 (V.35) Serial Pinout: ITU-TSS (CCITT) V.35 |
| --- |
| Male V.35 | Female V.35 |
| Pin | Signal Name | Abbreviation | V.24 Circuit Reference | Signal Direction |
| 1 | Shield | SHD | 101 | Ground |
| 2 | Signal Ground | SGND | 102 | Ground |
| 3 | Request to Send | RTS | 105 | Control, to DCE |
| 4 | Clear to Send | CTS | 106 | Control, from DCE |
| 5 | Data Set Ready | DSR | 107 | Control, from DCE |
| 6 | Received Line Signal Detector | RLSD | 109 | Control, from DCE |
| 7 | Data Terminal Ready | DTR | 108.2 | Control, to DCE |
| 8 | Calling Indicator | CI | 125 | Control, from DCE |
| 9 | Reserved for future international standards |
| 10 | Local Loopback | LL | 141 | Control, to DCE |
| 11 | Reserved for future international standards |
| 12 | Remote Loopback | RL | 140 | Control, to DCE |
| 13 | Send Data A | TD A | 103 | Data, to DCE |
| 14 | Receive Data A | RD A | 104 | Data, from DCE |
| 15 | Send Data B | TD B | 103 | Data, to DCE |
| 16 | Receive Data B | RD B | 104 | Data, from DCE |
| 17 | Serial Clock Transmit External A | SCTE A | 113 | Timing, to DCE |
| 18 | Serial Clock Receive A | SCR A | 115 | Timing, from DCE |
| 19 | Serial Clock Transmit External B | SCTE B | 113 | Timing, to DCE |
| 20 | Serial Clock Receive B | SCR B | 115 | Timing, from DCE |
| 21 | Serial Clock Transmit A | SCT A | 114 | Timing, from DCE |
| 22 | Reserved for future international standards |
| 23 | Serial Clock Transmit B | SCT B | 114 | Timing, from DCE |
| 24-28 | Reserved for future international standards |
| 29-32 | Reserved for country-specific standards |
| 33 | Reserved for future international standards |
| 34 | Test Mode | TM | 142 | Control, from DCE |

| Male DB15 | Female DB15 |
| --- | --- |
| Pin | Signal Name | X.21 Circuit Reference | V.24 Circuit Reference | Signal Direction |
| 1 | Shield | SHD | 101 | Ground |
| 2 | Transmit A | T (A) | 103 | Data, to DCE |
| 3 | Control A | C (A) | 105 | Control, to DCE |
| 4 | Receive A | R (A) | 104 | Data, from DCE |
| 5 | Indication A | I (A) | 109 | Control, from DCE |
| 6 | Signal Element Timing A | S (A) | 114 | Timing, from DCE |
| 7 | Byte Timing A | B (A) | N/A | Timing, from DCE |
| 8 | Signal Ground | G | 102 | Ground |
| 9 | Transmit B | T (B) | 103 | Data, to DCE |
| 10 | Control B | C (B) | 105 | Control, to DCE |
| 11 | Receive B | R (B) | 104 | Data, from DCE |
| 12 | Indication B | I (B) | 109 | Control, from DCE |
| 13 | Signal Element Timing B | S (B) | 114 | Timing, from DCE |
| 14 | Byte Timing B | B (B) | N/A | Timing, from DCE |
| 15 | Reserved for future international use |