Name:	Apple SSC

Type:	Super Serial Card

Short description:

The SSC gives the Apple ][ a serial port (RS232). Up to

19200 baud are possible. Full handshake is supported.

Installation:

The card plugs into Slot 1, 2 or 3 of the Apple. Slot 1 is

usually for a serial printer (Imagewriter), Slot 2 for a

modem and Slot 3 for a terminal.

The DB25 connector goes to the printer/modem/terminal line,

the 10-pin connector on the other side of the cable goes

into the cable socket at the rear side of the card.

Jumper settings:

The card has two jumpers and a additional jumper block.

The jumper block can be installed two ways:

1) Arrow pointing towards the word TERMINAL

2) Arrow pointing towards the word MODEM

Jumpered as MODEM, it will wire thru, jumpered as TERMINAL,

it will twist 2-3, 4-5 and 6-20 (called null modem).

The jumper switches are called SW1 and SW2, the switches

are numbered SW1-1 to SW1-7 and SW2-1 to SW2-7 from left

to right.

SW1-1	SW1-2	SW1-3	SW1-4

off	off	off	off	19200 baud

off	off	off	on	9600 baud

off	off	on	off	7200 baud

off	off	on	on	4800 baud

off	on	off	off	3600 baud

off	on	off	on	2400 baud

off	on	on	off	1800 baud

off	on	on	on	1200 baud

on	off	off	off	600 baud

on	off	off	on	300 baud

on	off	on	off	150 baud

on	off	on	on	135 baud

on	on	off	off	110 baud

on	on	off	on	75 baud

on	on	on	off	50 baud

SW2-1 off	2 stopbits

SW2-1 on	1 stopbit

SW2-2 off	no delay on carriage return

SW2-2 on	1/4 sec delay

SW2-3	SW2-4

off	off	132 chars/line, apple screen off

off	on	80 chars/line, apple screen off

on	off	72 chars/line, apple screen off

on	on	40 chars/line, apple screen on

SW2-5 off	no line feed after carrigae return

SW2-5 on	line feed

SW2-6 off	ignore interrupts

SW2-6 on	generate interrupts

SW1-7 on and SW2-7 off	pin 4 or 20 (clear to send)

SW1-7 off and SW2-7 on	in 19 (secondary clear to send)

DB-25 Pin assignment:

10-pin  DB-25

header  Connector       Signal name

------  ---------       ------------

1       1               Frame Ground

2       2               Transmit Data (TXD)

3       3               Receive Data (RXD)

4       4               Request to Send (RTS)

5       5               Clear to Send (CTS)

6       6               Data Set Ready (DSR)

7       19              Secondary Clear to Send (SCTS)

8       7               Signal Ground

9       20              Data Terminal Ready (DTR)

10      8               Data Carrier Detect (DCD)

Usage:

Register settings of the ACIA:

Memory locations used:

---------------------------------------------------------------------------

SUPER SERIAL CARD (SSC) SETUP SETTINGS

Recomended slots:

slot 1 for terminal use (e.g. printer)

slot 2 for communication use (e.g. modem)

Jumper Block:

for communication use label is upside down (arrow points up)

for terminal use label is right side up (arrow points down)

SW1 Dip Switch Settings:

Baud      SW1-1     SW1-2     SW1-3     SW1-4     SW1-8

50        on        on        on        off       not used

75        on        on        off       on        "

110       on        on        off       off       "

135       on        off       on        on        "

150       on        off       on        off       "

300       on        off       off       on        "

600       on        off       off       off       "

1200      off       on        on        on        "

1800      off       on        on        off       "

2400      off       on        off       on        "

3600      off       on        off       off       "

4800      off       off       on        on        "

7200      off       off       on        off       "

9600      off       off       off       on        "

19200     off       off       off       off       "

Switch Settings For Communication mode:

SW1-5; SW1-6; SW1-7 are all set on

Data          Parity    Stop      SW2-1     SW2-2     SW2-3     SW2-4

Bits                    Bits

7             none      1         on        off       off       on

7             odd       1         on        off       on        off

7             even      1         on        off       off       off

7             none      2         off       off       off       on

7             odd       2         off       off       on        off

7             even      2         off       off       off       off

8             none      1         on        on        off       on

8             odd       1         on        on        on        off

8             even      1         on        on        off       off

8             none      2         off       on        off       on

8             odd       2         off       on        on        off

8             even      1         on        on        off       off

8             none      2         off       on        off       on

8             odd       2         off       on        on        off

8             even      2         off       on        off       off

Note: SW2-1 thru SW2-4 settings can be overridden by software.

SW2-5:

ON  for linefeed out

OFF for no linefeed out

SW2-6:

ON for baud rates greater than 1199 baud

SW2-7:

OFF in communication mode

SW2-8:

Not used

Connector Pin Assignments

10-Pin    DB-25

Header    Connector          Signal Name

________________________________________________________________________

1         1               Frame Ground

2         2               Transmit Data (TXD)

3         3               Receive Data (RXD)

4         4               Request To Send (RTS)

5         5               Clear To Send (CTS)

6         6               Data Set Ready (DSR)

7        19               Secondary Clear To Send (SCTS)

8         7               Signal Ground

9        20               Data Terminal Ready (DTR)

10         8               Data Carrier Detect (DCD)