.The official Csa2 (comp.sys.apple2) Usenet newsgroup Apple II FAQs originate from   the GroundApple II site, 1997-1999. Ground Apple II administrator: Steve Nelson

.Csa2 FAQs-on-Ground ref: Csa2HDNSCSI.txt  rev016 6/25/1999

Hard Disks & SCSI Interfaces   Fto EntranceFto Contents

001- How difficult is it to add a hard drive to my IIgs?

002- What kinds of hard drive systems are available?

003- What do SCSI ID numbers mean?

004- What is "SCSI-2" and how is it different from SCSI-1?

005- Will a SCSI-2 hard drive work with an Apple II system?

006- Will my Rev. C SCSI Card work with a SCSI-2 drive?

007- What is SCSI "termination power"?

008- Can I avoid the "RamFAST/SCSI is searching SCSI bus" delay?

009- What is the pin-out for the standard 50-pin SCSI cable?

010- What's the SCSIHD.DRIVER patch to ignore DRIVER43 partitions?

011- What is the "bad bug" in the ROM 3.01e RamFAST?

012- What are correct HS SCSI settings, etc. for a Bernoulli drive?

013- What are the settings for a CMS hard drive controller card?

014- Does it matter when I power-ON my SCSI hard disk?

015- Can I leave SCSI devices I'm not using turned OFF?

016- Is there a generic SCSI tutorial available for downloading?

017- What is the correct time-out setting for a Focus hard drive?

018- How do I modify my Apple HSS card to supply Termination Power?

019- Can I get a Focus drive bigger than a couple hundred MB?

020- My hard disk is on a CMS SCSI. How do I install System 6.0.1?

021- How is DMA set for SCSI cards with 8MB RAM cards on the GS?

022- My 20MB Focus bombs and there's some goo on the card. A fix?

023- Where can I find the RamFAST manual on the net?

024- How can I tell which Apple SCSI card I have?

From: Bradley P. Von Haden

001- How difficult is it to add a hard drive to my IIGS?

Adding a hard drive is not much of a problem. Usually, you will need to insert

an interface card, possibly connect a cable or two, and change a Slot setting

in the Control Panel Desk Accessory.

---------------------------

002- What kinds of hard drive systems are available for Apple II

users?

The most versatile and most common hard drive set-up is an internal SCSI

interface card and an external SCSI drive.  Hard drives, cd-rom drives,

removable media (SyQuest, Iomega), flopticals, and scanners all can be added to

the SCSI chain.  Insert the card in a slot, connect a cable or two, and change

a slot setting.

The preferred SCSI card is the RamFAST Rev. D SCSI card from Sequential

Systems. The next best card is the Apple Hi-Speed SCSI card.

Here are some RamFAST notes:

- still being produced and supported by Sequential Systems

- faster than Apple Hi-Speed, especially in ProDOS

- provides termination power to the SCSI chain

- allows partitions to be mapped in ProDOS

- device drivers come on the card in the upgradeable ROM chip

(3.01f)

- allows up to 8 devices to be added to the chain

- allows up to 12 partitions to be active at any one time

(switchable)

- allows up to 12 partitions per drive

- about $130 new

Here are some Apple High Speed notes:

- no longer produced or supported by Apple

- does not provide termination power to the SCSI chain (can be

modified to provide termination power)

- does not allow partitions to be mapped in ProDOS

- device drivers are software

- allows up to 7 devices to be added to the chain

- allows over 100 partitions to be active at any one time

- allows up to 20 (?) partitions per drive

- about $110 new (if still available)

For the hard drive itself, look for a SCSI drive in an external

enclosure with the following features:

- 30 day money-back guarantee

- external SCSI ID switching

- dual 50 pin SCSI connectors

- no or switchable termination (use an external terminator at

end of SCSI chain)

- switchable termination power (on/off) is a plus for users of

SCSI interface cards which do not supply termination power

---------------------------

From: Rubywand

Another way to go is a 2.5" IDE drive mounted on an IDE interface card.

This "hard card" plugs into a Slot-- usually Slot 7. Alltech sells the Focus

Hard Card in varying sizes (e.g. 60MB for $99) with system software installed.

SHH Systeme offers the FileCard (about $170 + cost of drive) as well as a

series of IDE controller cards to which you can add a 2.5" IDE drive (about

$120-$170 including mounting kit).

The IDE hard card approach offers speed and capacity comparable to SCSI,

very easy installation, and, it eliminates hassles with external boxes and

cables. Of course, you will still need to add a SCSI interface card if you want

to connect a SCSI CD-ROM and/or Zip Drive.

Note: If you want your system to include a SCSI CD-ROM drive, it is best to

have a SCSI Zip Drive or SCSI hard disk connected to the SCSI interface, too.

This provides a write-able medium for saving SCSI interface card setup parms.

____________________________

From: Rubywand

003- What do the SCSI ID numbers mean?

SCSI ID numbers identify devices on the SCSI chain. Each device should

have its own, unique ID number in the range 0-7. (If two devices on the SCSI

chain have the same ID number, there will be a conflict and your system will

not function correctly.) Higher numbered devices have higher priority-- get

'looked for' first-- so, it is standard practice to set the device you boot

from to 6 or 7.

Most external SCSI devices have a thumbwheel switch, slide switch, or

jumper block on the back to set ID number. Some, like the Creative x2 CD-ROM

drive let you click through 0-7. The Zip Drive lets you pick 5 or 6. (By the

way, SCSI ID numbers have nothing to do with which Slot the SCSI interface card

is in.)

---------------------------

From: David Empson

SCSI ID 7 is usually special because the Apple SCSI and Hi-Speed SCSI

cards count as a device set to ID 7 by default (and every Macintosh has a

hard-wired SCSI ID of 7).  The only thing that is special about ID 0 is that it

is the standard ID used for an internal drive on a Macintosh.

There is no problem using SCSI ID 0 on an Apple II. On a RamFAST SCSI

card, it is also safe to use SCSI ID 7 for a drive. The RamFAST doesn't have a

SCSI ID, but every other SCSI card does.

___________________________

From: David Empson

004- What is "SCSI-2" and how is it different from SCSI-1?

For hard drives, "SCSI-2" basically means that the drive supports a stricter

command set. The physical interface is usually identical.

For other device types, "SCSI-2" means a lot more, because the original SCSI

standard didn't define much in the way of device types and command sets, so

most devices use proprietary command sets. SCSI-2 standardises the command sets

for most types of devices.

There are three special types of interface that you might see mentioned:

"Fast SCSI" supports data transfer at twice the speed of the  original SCSI

standard (10 MB per second vs 5 MB per second).  This  will not be a

compatibility issue, as it is just the maximum transfer  speed supported by the

drive.  The Apple II cannot transfer more than  one megabyte per second.

"Wide SCSI" uses a different cable arrangement to double the width of  the

data path (16 bits instead of 8 bits).  A wide SCSI drive cannot be  used with

an Apple II, unless it can also operated in "narrow" mode with  the original

50-pin connector.  (There is also "Fast Wide SCSI", which  doubles the data

rate and the width of the bus.)

"Differential SCSI" involves a different type of interface to the  computer,

where every data signal has a balanced positive and  negative pair of wires,

rather than a single wire and a ground line.  I believe it has a different type

of connector.  Differential SCSI  drives cannot be used with an Apple II."

Some drives use a proprietary connector, but the standard (narrow,

non-differential) SCSI bus uses the same 50-pin connector for SCSI-1 and

SCSI-2.

The only significant problem you might run into is termination, and supply of

termination power.  SCSI-2 devices tend to be fussier about termination than

older devices.

------------------------------

005- Will a SCSI-2 hard drive work with an Apple 2 system?

Usually, yes. I'm on my second Quantum drive that is described as

"SCSI-2".

There is a major caveat to this answer.  Some newer drives require a host

which implements the arbitration phase of the SCSI communication dialogue. The

RamFAST doesn't do this, and as a result there are some drives that cannot be

used with a RamFAST SCSI card. A notable example is the Quantum Fireball

series. However; the Trailblazer and all older Quantum models work fine.

------------------------------

006- I have a plain ol' Rev. C SCSI Card, will this work with a

SCSI-2 drive?

My Quantum LPS240 is working fine on an original Apple SCSI card.

Note: With the original Apple SCSI card, the card itself is not terminated, so

if you are connecting more than one device, you need to add a second terminator

between the computer and the first drive (using a "pass-through" external SCSI

terminator, or internal termination on the first drive).

------------------------------

007- What is SCSI "termination power"?

At least one device (SCSI card or any SCSI drive) must provide power for

the SCSI terminators by feeding 5 volts onto the TERMPWR line on the SCSI bus.

Usually, termination power is fed through a diode to prevent backfeeding

from a higher voltage source in case some other device is also supplying

termination power. A good implementation will have a fuse to protect against

shorts and a capacitor to cope with a sudden rise in termination power drain.

The Apple SCSI cards do not provide termination power (though some recent

Apple Hi-speed SCSI cards were modified by Apple to provide termination

power).  The RamFAST SCSI card can supply termination power.

If a drive can supply termination power, I recommend letting it do so. The

TERMPWR line can, in some cases, represent a significant load on the +5V rail

going to the Slots. Both of my Quantum drive mechanisms provide termination

power to the SCSI bus, avoiding the need to supply it from anywhere else.

----------------------------

From: Rubywand

On the RamFAST SCSI RevC card, DIP switch #1 is set to ON to supply

termination power. On other RamFAST SCSI cards, a jumper is placed at JP1 to

supply termination power.

According to RamFAST documentation, it is okay to have the card set to

supply termination power whether or not another device does with a few notable

exceptions. If a connected hard disk (e.g. a Sider drive) has a sticker saying

that the drive supplies termination power and that the interface must not, then

the RamFAST must be set to _not_ supply termination power.

____________________________

From: LJSilicon

008- I just reinstalled System 6.01. Now every time I cold boot

I get this message 'RamFAST/SCSI is searching the SCSI bus

for devices..etc.' and have to wait several seconds. WEIRD?!

When you reinstalled the software, the RamFAST set itself for a long

search. This is an option that you can change using the RamFAST utility. What

it is doing is giving your scsi devices a chance to spin up. If you want a fast

check, go to the options menu on the utilities and reset the Short Timeout

option there to "YES".

__________________________

From: David Empson

009- I would like to make my own SCSI cable. Does anyone on csa2

know the pin-out for the standard 50-pin SCSI cable?

The cable pinout is documented in the technical reference manual for the

Apple High-Speed SCSI card (and the original one as well).

This pinout is not a simple mapping from one end to the other.

I repeat that it is NOT easy to make one of these yourself.  Apart from any

issues of wiring errors, you also need a properly shielded cable to minimise

noise being picked up or radiated.  You should definitely not use a ribbon

cable.

Here is the pinout, assuming I haven't made any typos (I can't see any).

DB-25   50-pin     Function

1       49         -REQ

2       46         -MSG

3       50         -I/O

4       45         -RST

5       44         -ACK

6       43         -BSY

7       16,18,19   Ground lines

8       26         -DB0

9       20,21,22   Ground lines

10      29         -DB3

11      31         -DB5

12      32         -DB6

13      33         -DB7

14      1,2,3      Ground lines

15      48         -C/D

16      4,5,6      Ground lines

17      41         -ATN

18      7,8,9,11   Ground lines

19      47         -SEL

20      34         -DBP

21      27         -DB1

22      28         -DB2

23      30         -DB4

24      23,24,25   Ground lines

25      38         TERMPWR

The unlisted pins in the 50-pin connector (10, 12, 13, 14, 15,

17, 35, 36, 37, 39, 40, 42) are ground.

Note: the numbers for the 50-pin connector are counted along each

row, like a DB-25.  They are NOT the wire numbers in a ribbon cable.

____________________________

From: Steve Reeves

010- Is there some patch for SCSIHD.DRIVER to make it ignore

APPLE_DRIVER43 driver partitions?

Yes; you can change the counter in the string comparison routine that

checks for the "Apple_Driver" partition type string so that it only checks the

first 12 characters.  This counter is at byte $3574 in the System 6.0.1

SCSIHD.DRIVER file and is originally $1F.  Change this to $0B and the driver

will then ignore "Apple_Driver43" partitions.

If you make this or any other patch to the driver, I also you recommend

you bump up the version number.  Change byte $01FF from $10 to $2E (for version

6.02 experimental).

____________________________

from Harold Hislop

011- Someone told me there's supposed to be a bad bug in the

ROM 3.01e RamFAST. What is it?

Don't use the built in backup/restore in 3.01e!!! The restore opeation

will nuke the partition map on the drive being restored to, as well as all

existing partitions on that drive!

____________________________

From: Bradley VonHaden

012- What are correct HS SCSI settings, etc. for a Bernoulli drive?

My system is as follows:

ROM 1 Apple //gs

4mb AE RAM card

8mhz ZIP GS

Apple High-Speed SCSI card

90 mb Bernoulli hard drive

System 6.0.1

Three things I can think of to check:

One possibility is DMA compatibility.  If your memory card is not DMA

compatible, then switch 1 on the Apple HS SCSI card should be open (up).

Another possibility I guess is a SCSI ID conflict.  The Apple HS SCSI card's ID

at the factory is set to 7.  Here are the Apple HS SCSI card switch

combinations:

note1: Switch 1 controls DMA; open (up) turns DMA off

note2: Switches 2-4 control SCSI card ID

note3: 'U' means open (up), 'D' means closed (down),

'z' means Set for correct DMA (see note1)

SWITCH:     1234  1234  1234  1234  1234  1234  1234  1234

SETTING:    zUUU  zUUD  zUDU  zUDD  zDUU  zDUD  zDDU  zDDD

CARD ID:      0     1     2     3     4     5     6     7

Third, the scsi chain needs termination power to work properly.  This is

different from termination.  Both are required for a properly functioning scsi

chain.  It is possible that neither the Bernoulli drive nor the Apple HS SCSI

card is supplying termination power.  If this is the case, and there is no

other device on the scsi chain to supply said power, it probably won't work.

There is a modification (requires soldering skills) to the Apple HS SCSI card

to make it supply termination power.

____________________________

From: Jack Countryman IAC

013- I want to configure a CMS hard drive controller card to run a

20 meg drive for a //e. Could someone supply info on settings?

According to the CMS manual, page D3, the six sets of eight pairs of jumpers

(u1....u6) are for the following purpose:

_______________________________________________________________

/                                                               |

/     u 1          u 2            u 3            u 4       j2    |

/                                                                 |

/                                                                  |

|                                                                  |

|                                                                  |

|                                                                  |

|                                                                  |

|                                                                  |

|    u 5     u 6                                                   |

|___________________________________________                    j1 |

|                      |

|______________________|

u 1: Boot Scan delay....manual shows no jumpers here in default

configuration

u 2: first (left) jumper is 'Enable I.C.P. (Yes/No)', middle 6 not

used, last (right) is 'multiple initiators (Yes/No)'...manual

shows no jumpers in default configuration

u 3: Selection phase time out delay....I believe this sets how long

the card waits for the drive to come up to speed(?)...manual

shows the default as having 4, 5, and 7 with jumpers installed

u 4: Arbitration phase time out delay....manual shows default as no

jumpers installed

u 5: Bus Free phase time out delay...manual shows default as jumper

on number 1

u 6: Interrupt recovery delay....manual shows jumpers on 3, 4,

and 5

J1 and J2 are single sets of pins. The manual says J2 is not used,

but J1 is to be jumpered.

The card I have here, came out of a IIGS where it was hooked to first a

twenty meg CMS drive, and later a forty meg CMS drive.  It has the following

jumpers set:

u1:  jumper on 7

u2:  no jumpers

u3:  jumpers on 4, 5, and 7

u4:  no jumpers

u5:  jumper on 1

u6:  jumpers on 3, 4, and 5

j2:  no jumper

j1:  jumper

As I recall, this setup yeilded a rather long pause for the hard disk to

come up to speed (about 40 to 45 seconds) that we found necessary at the time

to avoid boot problems.

____________________________

From: B.J. Major

014- Does it matter when I power-ON my SCSI hard disk?

From the Apple IIgs Owner's Reference, page 267:

"In order for the Finder to recognize a hard disk, the hard disk must be

switched on and up to speed before you start up (or restart) the computer.

Switch on the hard disk, wait about 10 seconds for it to come up to speed, and

then restart the computer."

From the Macintosh User's Guide for desktop Macs, page 216:

"IMPORTANT:  Always turn on any external SCSI devices connected to your

Macintosh before turning on the computer itself.  Otherwise, your computer

cannot recognize the SCSI devices."

___________________________

From: Randy Shackelford

015- Can I leave SCSI devices I'm not using OFF when I

turn ON my GS?

If it were not okay, I would have fried plenty of hardware. I do this all

the time. I have seen no problems with having some devices off. As I have

mentioned, I keep my magneto optical off most of the time; and, my buddy who

uses my 700 now has a flatbed scanner and leaves it off most of the time. Both

work fine.

____________________________

From: Daniel L. Miller

Related FAQs Resources: R008SCSITUT.TXT (text)

016- Is there a generic SCSI tutorial available for downloading?

Yes. Bus signals, commands, etc. for the Small Computer Serial Interface

are described in the text resource file R008SCSITUT.TXT .

____________________________

From: Rubywand

017- What is the correct time-out setting for a Focus hard drive?

Supposedly, the purpose of having the Focus spin down and stop

after 2, 10, or whatever minutes of idleness is to prevent over-heating

and unnecessary wear. After a few days of trying various TO settings, I

set my "Time Out" to "Never" and have had no problems with over-heating

or crashes even after many all-day sessions.

----------------------------

Related FAQs Resources: R009HSSTMOD.GIF (GIF pic)

018- How do I modify my Apple Hi-Speed SCSI card to supply

Termination Power?

The Apple High Speed SCSI Termination Power modification consists of

adding a diode. It is shown in resource file R009HSSTMOD.GIF from Harold Hislop

and Dan Brown.

The pic shows a simple sketch of the back of the Apple High Speed SCSI card

near connectors 26-33. The directions say that you connect a 1N914 diode between

two points:

The anode (non-banded end) of the diode goes to the *top* of L1. The cathode

(banded/striped end) of the diode goes to the >bottom< of RP2

The pic shows the *top* of L1 to be a solder pad (just a solder pad with no trace

showing) a little ways up from a point between connectors 32 and 33.

The >bottom< of RP2 is just a bit up and to the left of the *top* of L1. It is

the lowest of several points (the pic shows 8) arranged in a vertical column

and should have a trace going off to the left.

____________________________

From: Scott G

019- Can I get a Focus drive bigger than a couple hundred MB?

Get a 40MB Focus Hard Card from Alltech.  Get an 800MB IDE 2.5" Quantum

GO-drive from Computer Shopper sources for pennies.  Replace the original drive

on the Focus Hard Card with the big one (VERY easy and self-explanatory, just

use a screw driver).  Low level format, partition, and high level format.

That's it!

___________________________

From: Gary Black

020- On my ROM-03 GS the hard disk is connected to a CMS SCSI card.

How do I install System 6.0.1?

It turns out that the SCSI drivers that come on the Sys 6.0.1 Install Disk

downloaded from ftp.apple.com are incompatible with CMS ver 3.0 (and probably

earlier) SCSI cards.

What I did was to replace scsi.manager and scsihd.driver in the System

6.0.1 Install disk SYSTEM/DRIVERS folder with scsi.manager, scsihd.driver, AND

CMS.driver from the CMS Utility disk.

With the replacement scsi drivers installed, the Install disk recognizes

the hard drive and installation went smoothly from that point. (The CMS files

are dated 1989 and 1990, so they are a bit older than the 6.01 files, which are

dated 1993. But, they work!)

____________________________

From: Scott G

021- How is DMA set for SCSI cards with 8MB RAM cards on the GS?

DMA needs to be turned off with the Apple HS SCSI card or the RamFAST

revision C card.  It does not need to be turned off with the RamFAST revision D

card (differentiated by being half sized).  All Sequential Systems RamFAST

cards are revision D as are late model CV Tech cards.  It is the RamFAST

revision D that is designed to DMA into any RAM card, even 8MB models. It was

made around the time of the CV RAM 8MB model that turned into Sequential's RAM

GS Plus, but functions just as well with the Sirius card.

____________________________

From: Louis Cornelio

022- My 20MB Focus bombs and there's some goo on the card. A fix?

The goo is leaking from the drive due to a failed seal which seems to

plague some of the older Conner drive modules. The fix is to check with the

seller of the drive for a replacement. At Alltech, a good Apple II person to

contact is Tony Diaz.

____________________________

From: Joe Walters

023- Where can I find the RamFAST manual on the net?

You can find it at several sites:

Plain text on-line readable at ...

ftp://209.180.253.179/cabi/FAQs.and.INFO/SCSIandIDE/

In a .SHK and/or binscii file at ...

ftp://ground.ecn.uiowa.edu/2/apple2/Docs/

ftp://apple2.caltech.edu/pub/apple2/miscinfo/

____________________________

From: Chuck Newby

024- How can I tell which Apple SCSI card I have?

The Apple High Speed SCSI card has a set of Dip Switches on it; the Rev C

doesn't, and the ROM chip date is older than 1989, if it shows at all.

The Apple SCSI cards older than REV C don't work in my IIe or IIgs......

----------------------------

From: Supertimer

The Apple High Speed SCSI card has a printed label on one of the chips

showing the name "Sandwich II" on it.

____________________________

F to top