ADT Null Modem Cable

Your cable may work as wired if you cross pins 7 & 8 of the PC side.

You are missing the additional handshaking signals that need to be

present (RTS/CTS) for hardware handshaking on the PC side that telecom

software needs.  Try this before reading on.

I made a handshaking modem cable for the IIc years back.  IIRC, when I

ran into the missing signals, I wired the DTR/DSR of the IIc into

RTS/CTS of the modem and then shorted the DTR/DSR/CD on the modem side.

This worked pretty slick for my friend.  She used a 14.4 modem with this

cable for quite some time.

If shorting 7 & 8 does not work, try this cable instead, it consists of

the modem cable I made long ago and a standard Null modem cable into one

wiring diagram.

Apple 5 Pin      PC 9 Pin

Pin 1 DTR ------ Pin 8 CTS

Pin 2 TD ------- Pin 2 RD

Pin 3 GND ------ Pin 5 GND

Pin 4 RD ------- Pin 3 TX

Pin 5 DSR ------ Pin 7 RTS

Pins 1 CD,4 DTR,6 DSR Shorted

The easiest ADT connection I have ever made was shorting pins 1 & 5 of

the IIc, hooking up TX, RX and Gnd (crossed) to the PC and shorted 7 &

8, then 1, 4 & 6.  This fooled all the signals and let it freewheel at

9600 baud.  Generally speaking, nothing is so slow that it can't keep up

with 9600 baud so i never ran into issues.  I tried this just to see if

it could be done, and it can.

If you have any problems following this, contact me off list and I'll

see what I can do.  (I own my own break-out box which makes this so much

easier.)