Apple IIgs & IIc Serial Connector Pinouts

EIA Standard RS-232C

1 1 1 1         1 1 1 1

1 2 3 4 5 6 7 8 9 0 1 2 3         3 2 1 0 9 8 7 6 5 4 3 2 1

_____________________________     _____________________________

o o o o o o o o o o o o o /      O O O O O O O O O O O O O /

\_o_o_o_o_o_o_o_o_o_o_o_o_/       \_O_O_O_O_O_O_O_O_O_O_O_O_/

1 1 1 1 1 1 2 2 2 2 2 2           2 2 2 2 2 2 1 1 1 1 1 1

4 5 6 7 8 9 0 1 2 3 4 5           5 4 3 2 1 0 9 8 7 6 5 4

Pin side                        Solder side

Male DB-25. Connector             Male DB-25. Connector

Pin    Signal Name            * Pin    Signal Name

1  Protective Ground          * 14  Secondary Transmitted Data

2  Transmitted Data (TXD)     * 15  Transmission Signal Element

3  Received Data  (RXD)       *      Timing (DCE Source)

4  Request to Send (RTS)      * 16  Secondary Received Data

5  Clear to Send (CTS)        * 17  Receiver Signal Element Timing

6  Data Set Ready (DSR)       * 18  Unassigned

7  Signal Ground (GND)        * 19  Secondary Request to Send (SCTS)

8  Received Line Detector     * 20  Data Terminal Ready (DTR)

9  Reserved for Data Testing  * 21  Signal Quality Detector

10  Reserved for Data Testing  * 22  Ring Detector

11  Unassigned                 * 23  Data Signal Rate Selector

12  Secondary Received Line    * 24  Transmit Signal Element Timing

Signal Detector           * 25  Unassigned

13  Secondary Clear to Send    *

(SCTS)                   *

======================================================================

Apple II, II+, IIe With Super Serial Card and DB-25 Connector (female)

Connector on Super Serial Card     Connector on cable to Printer

1 1 1 1                           1 1 1 1

3 2 1 0 9 8 7 6 5 4 3 2 1         3 2 1 0 9 8 7 6 5 4 3 2 1

_____________________________     _____________________________

O O O O O O O O O O O O O /      O O O O O O O O O O O O O /

\_O_O_O_O_O_O_O_O_O_O_O_O_/       \_O_O_O_O_O_O_O_O_O_O_O_O_/

2 2 2 2 2 2 1 1 1 1 1 1           2 2 2 2 2 2 1 1 1 1 1 1

5 4 3 2 1 0 9 8 7 6 5 4           5 4 3 2 1 0 9 8 7 6 5 4

Socket Pin side                      Solder side

Female DB-25. Connector            Male DB-25. Connector

Pin    Signal Name

1  Frame Ground

2  Transmit Data (TXD)

3  Receive Data (RXD)

4  Request to Send (RTS)

5  Clear to Send (CTS)

6  Data Set Ready (DSR)

7  Signal Ground (GND)

8  Data Carrier Detect (DCD)

19 Secondary Clear to Send (SCTS)

20 Data Terminal Ready (DTR)

======================================================================

Apple IIc with Din-5 Connector for Serial Printer/Modem Ports.(female)

Laser-128/128EX/128EX-2

Guide Notch                 Guide Notch

U                           U

*            *              *             *

*                   *        *                   *

O             O              O             O

* 5   O       O   1 *        * 5   O       O   1 *

4    O    2                  4    O    2

*     3      *              *      3      *

*                            *

Socket Pin Side                Solder side

Female Din-5 Connector        Male Din-5 Connector

On rear of Computer        On Cable to Printer/Modem

Pin    Signal Name, Same for both Printer/Modem Ports

1 Data Terminal Ready (DTR)

2 Transmit Data (TXD)

3 Ground (GND)

4 Receive Data (RXD)

5 Data Set Ready (DSR)

======================================================================

Apple IIgs Serial Printer/Modem Ports (Female)

Guide Notch                  Guide Notch

U                            U

*  8   7   6  *              *  8   7   6  *

O  O  O                      O  O  O

*                    *        *                   *

O  O  O                      O  O  O

*      5   4   3     *        *     5   4   3     *

O O                          O O

*    2   1    *              *    2   1    *

)   *   (                        *

Notch/. The notches are not seen from soldering side.

Socket Pin View                Solder side

Female Mini Din-8 Connector   Male Mini Din-8 Connector

On rear of Computer       On Cable to Printer/Modem

Pin    Signal Name, Same for both Printer/Modem Ports

1  Request to Send (RTS)  Handshake Out

2  Clear to Send (CTS)    Handshake in

3  Transmit Data- (TXD-)       #   -=[ Note ]=-

4  Signal Ground (GND)         #   TXD- and RXD-

5  Receive Data- (RXD-)        #   TXD+ and RXD+ (not normally used)

6  Transmit Data+ (TXD+)       # May relate to the Laser Writer

7  Data Carrier Detect (DCD)   # that uses the DB-9 Connector. I

8  Receive Data+ (RXD+)        # need more input on this.

======================================================================