Apple IIgs Serial Connector Pinout

Looking at the IIgs serial connector, the pins are numbered as follows:

8   7   6

5   4   3

2   1

The signals on each pin are:

1  Handshake Out (DTR)

2  Handshake In (DSR)

3  Transmit Data minus

4  Signal Ground

5  Receive Data minus

6  Transmit Data plus

7  General purpose input (DCD)

8  Receive Data plus

Shield is frame ground.

The ImageWriter I or DeskJet 500 has a female DB-25 connector,

arranged in the standard order for a DTE (Data Terminal Equipment), i.e.

1  Frame Ground

2  Transmit Data

3  Receive Data

4  Request to Send (output from printer, probably not used)

5  Clear to Send (input to printer, probably not used)

6  Data Set Ready (input to printer)

7  Signal Ground

8  Carrier Detect (input to printer, probably not used)

20 Data Terminal Ready (output from printer)

The pinout of the cable is:

IIgs (Mini-Din-8 male)       Printer (DB-25 male)

1 (HShk Out)                 6  (DSR)

2 (HShk In)                  20 (DTR)

3 (TxD-)                     3  (RxD)

4 (Gnd)                      7  (Gnd)

5 (RxD-)                     2  (TxD)

6 (TxD+)  no connection

7 (DCD)   no connection

8 (RxD+)  must be conected to signal ground (IIgs pin 4, printer pin 7)

If you have a shielded cable, also connect the cable shield to the

Mini-Din-8 plug's shielding, and to pin 1 and the shield of the DB-25.