DB-9 ( Mini Din-8 pinout

For direct cable connection between Apple IIgs/IIc+ and PC

First built by Terry R. Olsen, aka Tall Runner

Tolsen64@hotmail.com

| Din-8 | Din-8 | Apple Iigs/c+ | Windows Box | DB-9 | DB-9 |
| --- | --- | --- | --- | --- | --- |
| Signal | Signal Function/Direction | Din-8 | DB-9 Female | Signal | Signal Function/Direction |
| Handshake Output (DTR) | Control, to DCE | 1 | 8 | Clear to Send (CTS) | Control, from DCE |
| Handshake Input (DSR) | Control, from DCE | 2 | 7 | Request to Send (RTS) | Control, to DCE |
| Transmitted Data (Minus) | Data, to DCE | 3 | 2 | Received Data | Data, from DCE |
| Signal Ground | Ground | 4 | 5 | Signal Ground | Ground |
| Received Data (Minus) | Data, from DCE | 5 | 3 | Transmitted Data | Data, to DCE |
| General Purpose Input (DCD) | Control, from DCE | 7 | 4 | DTE Ready | Control, from DCE |

Pin 7 of the Apple IIgs port is used for carrier detect.  When pin 4 of the Windows Box goes low, it will cause the BBS running on the Apple IIgs to see a “dropped carrier” and the BBS will reset.

Pins 6 & 8 of the Apple IIgs port are not used.

I used the shielding. Whether that makes a difference or not, I don’t know.