Metal/FV: Cable and Pinouts

------------------------------------------

All you need for a GS/MAC to a HI-SPEED MODEM (using RTS/CTS) is as follows:

------------------------------------------

GS PORT CONNECTOR               RS-232C CONNECTOR

(Male mini-8)                   (Male DB-25)

-----------------               ----------------

Pin 1: HSKo ------------------> Pin 4: RTS   GS Drops HSKo to have mdm stop

Pin 2: HSKi <------------------ Pin 5: CTS   MDM Drops CTS to have GS stop

Pin 3: TxD- ------------------> Pin 2: TD

Pin 4: SG   <-----------------> Pin 7: SG

Pin 5: RxD- <------------------ Pin 3: RD

Pin 6: TxD+  **NO CONNECTION**

Pin 7: GPi  <------------------ Pin 8: DCD   Carrier Detection using &C1

Pin 8: RxD+  **NO CONNECTION**               (NORMAL CARRIER DETECT!)^^^

[Arrows show signal direction-- Connect them both at specified pins]

Set your Control Panel Setting for the defaults EXCEPT for DCD Handshake: NO and BUFFERING: ON

Set your USRobotics or similar modem so that:

DIP SWITCH #1 on USR HST: DOWN (ON): DTR ALWAYS ON  (otherwise commands will NOT be recognized (Check manual for switch)

--------------------------------------------------------------------------------

If you are using a IIgs and its modem port, the following is the right and

proper cable. Pay attention Apple!!!

Here is the correct cable pinout for the Apple IIGS modem port.

DB-25 End     Mini DIN 8 End

----------------------------

2   <---------<    3  TX-

3   >--------->    5  RX-

6   >--------->    2  DSR (handshake in)

20   <---------<    1  DTR (handshake out)

8   >--------->    7  DCD

7   ------+----    4  SIG GND

|

+---->   8  RX+

Ground RX+ to prevent noise pickup, it isn't needed for RS-232.

Pin 6, TX+, is not connected to anything.

Hope this helps, if you need more information, email mdavis@pro-sol.cts.com

he's tthe best expert on GS telecom.