- 1 -       ZMODEM PROTOCOL REFERENCE                                   The                                  ZMODEM                            Inter Application                          File Transfer Protocol                              Chuck Forsberg                 Please distribute as widely as possible.                       Questions to Chuck Forsberg                           Omen Technology Inc                   17505-V Northwest Sauvie Island Road                          Portland Oregon 97231                           Voice: 503-621-3406            Modem (Telegodzilla): 503-621-3746 Speed 1200,300                          Compuserve: 70715,131                    UUCP: ...!tektronix!reed!omen!caf                                  - 2 -       1.  ACKNOWLEDGMENTS       Encouragement and suggestions by Stuart Mathison, Thomas       Buck, John Wales, Ward Christensen, and Irv Hoff are       gratefully acknowledged.       2.  ROSETTA STONE       Here are some definitions which reflect the current       vernacular in the computer media.  The attempt here is       identify the file transfer protocol rather than specific       programs.       Frame   A ZMODEM frame consists of a header packet and 0 or               more data packets.       Response Time This is the maximum expected delay between the               receiver sending a packet to the transmitter and               receiving the beginning of a response from the               transmitter.       XMODEM  refers to the original 1979 file transfer etiquette               introduced by Ward Christensen's 1979 MODEM2               program.  It's also called the MODEM or MODEM2               protocol.  Some who are unaware of MODEM7's unusual               batch file mode call it MODEM7.  Other aliases               include "CP/M Users's Group" and "TERM II FTP 3".               This protocol is supported by every serious               communications program because of its universality,               simplicity, and reasonable performance.       XMODEM/CRC replaces XMODEM's 1 byte checksum with a two byte               Cyclical Redundancy Check (CRC-16), giving modern               error detection protection.       YMODEM  refers to the XMODEM/CRC protocol with the               throughput and/or batch transmission enhancements               described in YMODEM.DOC.       ZMODEM  Zmodem is a second generation streaming protocol for               text and binary file transmission between               applications running on microcomputers and               mainframes.       Chapter 3              DRAFT 3-24-86                       2       DRAFT ZMODEM Protocol Ref 02-23-86                         3       3.  YET ANOTHER PROTOCOL, AGAIN?       Since its development half a decade ago, the Ward       Christensen modem protocol has enabled a wide variety of       computer systems to interchange data.  There is hardly a       communications program that doesn't at least claim to       support this protocol now called XMODEM.       Advances in computing, modems and networking have spread the       XMODEM protocol far beyond the close coupled micro to micro       environment for which it was designed.  These application       have exposed some weaknesses.          o+ The short block length causes throughput to suffer when            used with timesharing systems, packet switched            networks, satellite circuits, and buffered (error            correcting) modems.          o+ The 8 bit arithmetic checksum and other aspects allows            line impairments to interfere with dependable, accurate            transfers.          o+ Only one file can be sent per command.  The file name            has to be given twice, first to the sending program and            then again to the receiving program.          o+ The transmitted file accumulates as many as 127            extraneous bytes.          o+ The modification date of the file is lost.       A number of other protocols have been developed over the       years, but none have displaced XMODEM to date.          o+ Lack of public domain documentation and example            programs have kept proprietary protocols such as MNP,            Blast, and others tightly bound to the fortunes of            their suppliers.          o+ Hardware and/or software complexity discourages the            widespread application of BISYNC, SDLC, HDLC, X.25, and            X.PC protocols.          o+ Link level protocols such as X.25, X.PC, and MNP modems            do not manage application to application file            transfers.          o+ The Kermit protocol was developed to allow file            transfers in environments hostile to XMODEM.  The            performance compromises necessary to accomodate non            transparent environments limit Kermit's efficiency.       Chapter 3              DRAFT 3-24-86                       3       DRAFT ZMODEM Protocol Ref 02-23-86                         4            Even with completely transparent channels, Kermit            control character quoting limits the efficiency of            binary file transfers to about 75 per cent.            Kermit Sliding Windows ("SuperKermit") improves            throughput over networks at the cost of increased            complexity.  SuperKermit state transitions are encoded            in a special language "wart" which requires a C            compiler.  The SuperKermit C code requires full duplex            communications and the ability to check for the            presence of characters in the input queue, precluding            its implementation on some operating systems.       A number of extensions to the XMODEM protocol have been made       under the collective name YMODEM.        o+ YMODEM-k reduces the overhead from transmission delays by          87 per cent compared to XMODEM, but network delays can          still degrade performance.        o+ The handling of files that are not a multiple of 1024 or          128 bytes is awkward, especially if the file length is          not known, or changes during transmission.        o+ YMODEM-g is essentially insensitive to network delays.          Because it does not support error recovery, YMODEM-g must          be used hardwired or with a link level protocol.       Another XMODEM "extension" is protocol cheating, referred to       as "Turbo Download" and OverThruster.  These improve XMODEM       throughput at the expense of error recovery.       The ZMODEM Protocol is proposed as a means of addressing the       weaknesses described above while maintaining as much of       XMODEM's simplicity and prior art as possible.       4.  ZMODEM Protocol Design Criteria       The design of a file transfer protocol is an engineering       compromise between conflicting requirements:       4.1  Throughput       ZMODEM is designed for optimum performance with minimum       degradation caused by delays introduced by packet switched       networks and timesharing systems.       ZMODEM is optimized for best throughput where line hits       occur infrequently.  This assumption markedly reduces code       Chapter 4              DRAFT 3-24-86                       4       DRAFT ZMODEM Protocol Ref 02-23-86                         5       complexity and memory requirements.       It is assumed that many transfers will originate from a       timesharing system connected to a packet switched network.       ZMODEM provides features to allow for simple, efficient       implementation on timesharing hosts.       File transfers begin immediately regardless of which program       is started first, no 10 second delay.       4.2  Integrity and Robustness       All packets are protected with 16 bit CRC.       4.3  Ease of use       File names need be entered only once.  Wild Card names may       be used with batch transfers.  Minimum keystrokes required       to initiate transfers.  ZMODEM steps down to X/YMODEM if the       other end does not support ZMODEM.       4.4  Ease of implementation       ZMODEM accomodates a wide variety of systems:        o+ Microcomputers that cannot overlap disk and serial i/o        o+ Microcomputers that cannot overlap serial send and          receive        o+ Computers and/or networks requiring XON/XOFF flow control        o+ Computers that cannot check the serial input queue for          the presence of data without having to wait for the data          to arrive.       Although ZMODEM provides "hooks" for multiple "threads",       ZMODEM is not intended to replace link level protocols such       as X.25.  ZMODEM provides a near optimal general purpose       application to application file transfer protocol to be used       with link level protocols such as X.25, MNP, Fastlink, etc.       5.  PACKETIZATION       ZMODEM uses packets somewhat different from those used in       X/YMODEM.  X/YMODEM type packets are not used for the       following reasons:        o+ Block numbers are limited to 256       Chapter 5              DRAFT 3-24-86                       5       DRAFT ZMODEM Protocol Ref 02-23-86                         6        o+ No provision for variable length blocks        o+ Line hits corrupt protocol signals, causing failed file          transfers.  In particular, modem errors sometimes          generate false block numbers, false EOTs and false ACKs.          False ACKs are the most troublesome as they cause the          sender to lose synchronization with the receiver.          State of the art X/YMODEM programs such as Professional-          YAM overcome some of these weaknesses with clever          proprietary code, but a newer protocol is still useful.        o+ It is difficult to determine the beginning and ends of          X/YMODEM blocks when they are corrupted by line hits.          This discourages rapid error recovery.       5.1  Link Escape Encoding       ZMODEM acheives data transparency by extending the 8 bit       character set (256 codes) with escape sequences based on the       ZMODEM data link escape character ZDLE.1       Link Escape coding permits variable length data packets.  It       allows the beginning of packets to be detected without       special timing techniques, facilitating rapid error       recovery.       Link Escape coding does add some overhead.  The worst case,       a file consisting entirely of ZDLE characters, would incur a       50% overhead.  The particular ZDLE character was chosen       after examining the character distributions of many types of       files used with personal computers.       The ZDLE character is special.  ZDLE represents a control       sequence of some sort.  If a ZDLE character appears in the       data sent within a binary packet, it is prefixed with       another ZDLE.  An escaped ZDLE is counted once in the CRC.       The current value for ZDLE is exclamation point (!).  Use of       a printing character as ZDLE allows application programs to       recognize HEX Header Packets.  This particular character was       chosen because it does not appear often in many types of       files likely to be transferred with this protocol.  In       __________        1. This and other constants are defined in the _z_m_o_d_e_m._h           include file.  Please note that constants with a leading           0 are octal constants in C.       Chapter 5              DRAFT 3-24-86                       6       DRAFT ZMODEM Protocol Ref 02-23-86                         7       addition, no known timesharing system uses it for editing.       5.2  Header Packet Information       All ZMODEM frames begin with a header packet which may be       sent in binary or HEX form.  ZMODEM uses a single routine to       recognize binary and hex header packets.  Either form of the       header packet contains the same raw information:        o+ A type byte 2 Future extensions to ZMODEM may use the          high order bits of the type byte to indicate thread          selection.        o+ Four bytes of data indicating flags and/or numeric          quantities depending on the packet type                   Order of Bytes in Header Packet                   T:  packet Type                   F0: Flags least significant byte                   P0: file Position least significant                   P3: file Position most significant                           T  F3 F2 F1 F0                           --------------                           T  P0 P1 P2 P3       5.3  Binary Header Packet       A binary header packet is only sent by the sending program       to the receiving program.       A binary header packet begins with the sequence ZPAD, ZDLE,       ZBIN.       The frame type byte is ZDLE encoded.       The four position/flags bytes are ZDLE encoded.       A two byte CRC of the frame type and position/flag bytes is       ZDLE encoded.       0 or more binary data packets will follow depending on the       __________        2. The packet types are cardinal numbers beginning with 0           to minimize state transition table memory requirements.       Chapter 5              DRAFT 3-24-86                       7       DRAFT ZMODEM Protocol Ref 02-23-86                         8       frame type.       The function _z_s_b_h_d_r transmits a binary header packet.  The       function _z_g_e_t_h_d_r receives a binary or hex header packet.       5.4  HEX Header Packet       The receiver sends responses in hex header packets.       Hex encoding is required to support XON/XOFF flow control.       Use of Kermit style encoding for control and paritied       characters was considered and rejected because of increased       possibility of interacting with some timesharing systems's       line edit functions.  Use of HEX packets from the receiving       program allows control characters to be used to interrupt       the sender when errors are detected.  Except for header       packet types that imply data packets to follow, a HEX header       packet may be used in place of a binary header packet.       A hex header packet begins with the sequence ZPAD, ZPAD,       ZDLE, ZHEX.  The _z_g_e_t_h_d_r routine synchronizes in the ZPAD-       ZDELE sequence.  The extra ZPAD allows other parts of the       program to detect a ZMODEM packet and then call _z_g_e_t_h_d_r to       receive the packet.       The type byte, the four position/flag bytes, and the CRC       thereof are sent in hex using the character set       01234567890abcdef.  Upper case hex digits are not allowed;       they would false trigger X/YMODEM programs.       A carriage return, line feed, and XON are appended to the       HEX header packet but are not considered to be part of it.       The CR/LF aids debugging from printouts.  The XON releases       the sender from spurious XOFF flow control characters       generated by line noise, a common occurrence.       0 or more HEX data packets will follow depending on the       frame type.       The function _z_s_h_h_d_r sends a hex header packet.       5.5  Binary Data Packets       Binary data packets immediately follow the associated binary       header packet.  A binary data packet contains 0 to 1024       bytes of data.  Recommended length values are 256 bytes       below 4800 bps, 1024 above 4800 bps or when the data link is       known to be relatively error free.       No padding is used with binary data packets.  The data bytes       Chapter 5              DRAFT 3-24-86                       8       DRAFT ZMODEM Protocol Ref 02-23-86                         9       are ZDLE encoded and transmitted.  A ZDLE and frameend are       then sent, followed by two ZDLE encoded CRC bytes.  The CRC       accumulates the data bytes and frameend.       The function _z_s_b_d_a_t_a sends a binary data packet.  The       function _z_r_b_d_a_t_a receives a binary data packet.       5.6  HEX Data Packet       The format of HEX data packets is not currently specified.       These would be used for server commands, etc.       6.  PROTOCOL TRANSACTION OVERVIEW       As with the XMODEM recommendation, ZMODEM timing is receiver       driven.  The transmitter should not time out at all, except       to abort the program if no packets are received for an       extended period of time, say one minute.       To start a ZMODEM file transfer session, the sending program       is called with the names of the desired file(s).       The sending program sends the string "rz\r" and a single HEX       ZRQRINIT packet with data = 0.  The "rz" followed by       carriage return activates a ZMODEM receive program or       command if it were not already active.  If the receiving       program receives the ZRQRINIT packet, it totally ignores it       as the sending program will be responding to the RINIT       packet sent by the receiver.  The sending program should       also ignore this packet type, which would be an echo of its       own packet.       Since the ZRQRINIT sequence contains no exotic control       characters, it can be accepted by the application program as       a command to begin ZMODEM receive.  The sequence prints as       "rz^M**!B00000000000000^M^J" where ^M represents CR and ^J       represents LF.       The sending program awaits a command from the receiving       program to start file transfers.  If a "C" or NAK is       received, an XMODEM or YMODEM file transfer is indicated,       and file transfer(s) use the X/YMODEM protocol.  Note: With       ZMODEM and YMODEM Batch, the sending program provides the       file name, but not with XMODEM.       When the ZMODEM receive program starts, it immediately sends       a ZRINIT packet to initiate ZMODEM file transfers.  The       receive program resends the ZRINIT packet at _r_e_p_s_o_n_s_e _t_i_m_e       intervals for a suitable period of time (40 seconds typical)       Chapter 6              DRAFT 3-24-86                       9       DRAFT ZMODEM Protocol Ref 02-23-86                        10       before falling back to X/YMODEM protocol.  If the receiving       program receives a ZRINIT packet, it is an echo indicating       that the sending program is not operational.       If the receiving program receives a ZRQRINIT packet, it       ignores it.       Eventually the sending program correctly receives the ZRINIT       packet.              The sender may respond with an optional              ZCRYPT packet, which the receiver              acknowledges with a suitable frame.  (Details              to be worked out later)       The sender may respond with an optional ZSINIT frame to set       the receiving program's Attention string.  The receiver       sends a ZACK packet in response.       The sender then sends a ZFILE packet containing the file       name, file length, modification date, and other information       identical to that used by YMODEM Batch.              The receiver may respond to this with a              ZGETCRC packet, which requires the sender to              permorm a CRC on the file and transmit same              with a ZCRC packet.  The receiver may use              this information to determine whether to              accept the file or skip it.       The receiver may respond with a ZSKIP packet, which causes       the file to be passed over.       A ZRPOS packet from the receiver initiates transmission of       the file data starting at the offset in the file specified       in the ZRPOS packet.  Normally the receiver specifies the       data transfer begin begin at offset 0 in the file.              The receiver may start the transfer further              down in the file.  This allows a file              transfer interrupted by a loss or carrier              or system crash to be completed on the next              connection without requiring the entire              file to be retransmitted.  If downloading a              file from a timesharing system that becomes              sluggish, the transfer can be interrupted              and resumed later with no loss of data.       The sender sends a ZDATA header packet (with file       position) followed by one or more data packets.       The receiver compares the file position in the ZDATA       Chapter 6              DRAFT 3-24-86                      10       DRAFT ZMODEM Protocol Ref 02-23-86                        11       header with the number of characters successfully       received to the file.  If they do not agree, a ZRPOS       error response is generated to force the sender to the       right position within the file.       A data packet terminated by ZCRCGO and CRC does not       elicit a response unless an error is detected; more data       packet(s) follow immediately.              ZCRCQ data packets expect a ZACK response              (with the file offset) if no error,              otherwise a ZRPOS response (with the last              good file offset).  Another data packet              continues immediately.  ZCRCQ packets are              not used if the receiver does not indicate              FDX ability with the CANFDX bit.       ZCRCW data packets expect a response before the next       frame is sent.  If the receiver does not indicate       overlapped I/O capability with the CANOVIO bit, the       sender uses the ZCRCW to allow the receiver to write its       buffer before sending more data.              A zero length data packet may also be              used as a sending idle packet to prevent              the receiver from timing out in case data              is not immediately available to the              sender.       In the absence of fatal error, the sender encounters       end of file.  If the end of file is encountered within       a frame, the frame is closed with a ZCRCE data packet       which does not elicit a response except in case of       error.       The sender sends a ZEOF packet with the file ending       offset equal to the number of characters in the file.       The receiver compares this number with the number of       characters received.  If the receiver has received all       of the file, it closes the file and responds with       ZRINIT.  Otherwise the receiver sends ZRPOS with the       current file offset, forcing the sender to send the       missing data.       After all files are processed, any further protocol       errors should not prevent the sending program from       returning with a success status.       The sender closes the session with a ZEXIT header       packet.  The receiver acknowledges this with its own       ZEXIT packet.       Chapter 6              DRAFT 3-24-86                      11       DRAFT ZMODEM Protocol Ref 02-23-86                        12       When the sender receives the acknowledging packet, it       sends two characters, "OO" (Over and Out) and exits to       the operating system or application that invoked it.       The receiver waits briefly for the "O" characters, then       exits whether they were received or not.       7.  STREAMING TECHNIQUE       ZMODEM allows a choice of data streaming methodmethods       selected according to the limitations of the sending       program operating environment, receiving program       operating environment, and the transmission channel(s).       If the computers can overlap serial I/O with disk I/O,       the sender begins data transmission with a ZDATA header       and continuous ZCRCG data packets.  When the receiver       detects an error, it sends the Attn sequence and a       ZRPOS packet to force the sender back to the correct       position within the file.       At the end of each transmitted packet, the sender       checks for the presence of a error packet from the       receiver.  To do this, the sender may sample the       reverse data stream for the presence of a ZPAD       character.       If the reverse data stream cannot be sampled without       entering an I/O wait, the receiver can interrupt the       sender with a control character, break, or combinations       thereof, as specified in the ZSINIT frame sent by the       sending program.       If the receiver cannot overlap serial and disk I/O, it       uses the ZRINIT frame to specify a buffer length which       the sender will not overfill before sending a ZCRCW       packet.       8.  ATTENTION SEQUENCE       The receiving program sends the Attn sequence whenever       it detects an error and needs to interrupt the sending       program.       The default Attn string value is empty (no Attn       sequence).  The characters in the Attn string are       terminated with a null.  Two characters perform special       functions:       Chapter 8              DRAFT 3-24-86                      12       DRAFT ZMODEM Protocol Ref 02-23-86                        13          o+ \335 Sends a break signal          o+ \336 Pauses one second       9.  PACKET/FRAME TYPES       The numeric values for the values shown in boldface are       given in _z_m_o_d_e_m._h.       9.1  ZRQRINIT       Sent by the sending program to call up the receiving       program.  P0...P3 are zero.       9.2  ZRINIT       Sent by the receiving program.  ZF0 and ZF1 contain       receiver capability flags:       #define CANFDX  1 /* Rx can send and receive FDX */       #define CANOVIO 2 /* Rx can receive during disk I/O */       #define CANBRK  4 /* Rx can send a break signal */       #define CANCRY  8 /* Receiver can decrypt */       ZP0 and ZP1 contain the size of the receiver's buffer       in bytes, or 0 if overlapped I/O is allowed.       9.3  ZSINIT       Sender sends capability flags (none currently defined)       followed by a binary data packet terminated with ZCRCW.       Data contains the Attn string, maximum length 32 bytes.       The ZSINIT is only sent to programs that indicate the       ability to overlap serial data and disk I/O (CANOVIO).       9.4  ZACK       Acknowedgement to ZSINIT header packet or ZCRCW data       packet.  ZP0 to ZP3 contain file offset.       9.5  ZFILE       This packet indicates the beginning of a file       transmission attempt.  ZF0 and ZF1 contain special file       processing flags:        o+ ZBIN This is a binary file       A ZCRCW data packet follows with file name, file       length, modification date, and other information       described in a later chapter.       Chapter 9              DRAFT 3-24-86                      13       DRAFT ZMODEM Protocol Ref 02-23-86                        14       9.6  ZSKIP       Sent by the receiver in response to ZFILE, makes the       sender skip to the next file.       9.7  ZNAK       Indicates last packet header was garbled.  (See also       ZRPOS).       9.8  ZABORT       Sent by receiver to terminate batch file transfers when       requested by the user.  Sender initiates a ZFIN       sequence.1       9.9  ZFIN       Sent by sending program to terminate ZMODEM.  Receiver       responds with ZFIN.       9.10  ZRPOS       Sent by receiver to force file transfer to resume at       file offset given in ZP0...ZP3.       9.11  ZDATA       ZP0...ZP3 contain file offset.  One or more data       packets follow.       9.12  ZEOF       ZP0...ZP3 contain file offset.  Sender reports End of       File.       9.13  ZFERR       Error in reading or writing file, equivalent to ZABORT.       __________        1. Or ZCOMPL in case of server mode.       Chapter 9              DRAFT 3-24-86                      14       DRAFT ZMODEM Protocol Ref 02-23-86                        15       9.14  ZCRC       Request (receiver) and response (sender) for file CRC.       ZP0 and ZP1 contain 16 bit file CRC.       9.15  ZCRYPT       Negotiation for encryption.       9.16  ZCOMPL       Server request now completed.       10.  Transaction       A simple transaction, one file, no errors, overlapped       I/O:       Sender          Receiver                       ZRINIT       ZFILE                       ZRPOS       ZDATA data ...       ZEOF                       ZRINIT       ZFIN                       ZFIN       OO       11.  PERFORMANCE       Some tests of ZMODEM protocol performance have been       made.  A PC-AT with SCO SYS V Xenix or DOS 3.1 was       connected to a PC with DOS 2.1 either directly at 9600       bps or with dial-up 1200 bps modems.  The ZMODEM       software was configured to use 1024 byte packet lengths       above 2400 bps, 256 otherwise.       Because no time delays are necessary in normal file       transfers, per file negotiations are much faster than       Chapter 11             DRAFT 3-24-86                      15       DRAFT ZMODEM Protocol Ref 02-23-86                        16       with YMODEM, the only observed impidiment being the       time required by the program(s) to update logging       files.       During a file transfer, a short line hit seen by the       receiver usually induces a CRC error.  The interrupt       packet is usually seen by the sender before the next       packet is sent, and the resultant loss of data       throughput averages about half a packet.  At 1200 bps       this is would be about .75 second lost per hit.  At       10-5 error rate, this would degrade throughput by about       9 per cent.  The throughput degradation increases with       the channel delay, as the packets in transit through       the channel are discarded on error.       A longer noise burst that affects both the receiver and       the sender's reception of the interrupt packet usually       causes the sender to remain silent until the receiver       times out in 10 seconds.  If the round trip channel       delay exceeds the receiver's 10 second timeout,       recovery from this type of error may become difficult.       Noise affecting only the sender is usually ignored,       with one common exception.  Spurious XOFF characters       generated by noise stop the sender until the receiver       times out and sends an interrupt packet which concludes       with an XON.       In summation, ZMODEM performance in the presence of       errors resembles that of X.PC and SuperKermit.  Short       bursts cause minimuml data loss.  Long bursts (such as       pulse dialing noises) often require a timeout error to       restore the flow of data.       12.  TABLES                 Figure 1.  Protocol Overhead Information       Figures are calculated for round trip delay times of 40       milliseconds and 5 seconds.  A 102400 byte randomly       distributed binary file is sent at 1200 bps 8 data       bits, 1 stop bit.  The calculations assume no       transmission errors.  For each of the protocols, only       the per file functions are considered.  Processor and       I/O overhead are not included.  YM-k refers to YMODEM       with 1024 byte packets.  YM-g refers to the YMODEM "g"       option.  ZMODEM uses 256 byte packets for this example.       SuperKermit uses amximum packet size, 8 bit transparent       Chapter 12             DRAFT 3-24-86                      16       DRAFT ZMODEM Protocol Ref 02-23-86                        17       transmission, no run length compression.        Protocol     dump   XMODEM   YM-k    YM-G   ZMODEM   S-Kermit       Round-Trips   -      803      103     5      5        5?       Time@40ms     -      32s      4s      -      -        -       Time@5s       -      4015s    515s    25s    25s      25       Chars-Ovhd    -      4803     603     503    2000     7460       Time@0s       853s   893s     858s    857s   870s     1135s       Time@40ms     853s   925s     862s    857s   870s     1135s       Time@5s       853s   5761s    1373s   882s   905s     1160s                 Figure 2.  Transmission Time Comparision       (5 second delay)       **********************************************************       XMODEM       ************** YMODEM-K       ************ Kermit Sliding Windows       ********* YMODEM-G       ********* ZMODEM               Figure 3.  Y/ZMODEM Header Information usage        Program     Batch   Length   Date   Mode   S/N   YMODEM-g   ZMODEM       Unix rb/sb   yes     yes      yes    yes    no    sb only    no       Unix rz/sz   yes     yes      yes    yes    no    sb only    yes       VMS rb/sb    yes     yes      no     no     no    no         no       Pro-YAM      yes     yes      yes    no     yes   yes        yes       CP/M YAM     yes     no       no     no     no    no         no       KMD/IMP      yes     no|-      no     no     no    no         no       MEX          no      no       no     no     no    no         no       13.  ZFILE FRAME FILE INFORMATION       Only the pathname (file name) part is required for       batch transfers.       Pathname The pathname (conventionally, the file name)            is sent as a null terminated ASCII string.  This            is the filename format used by the handle oriented            MSDOS(TM) functions and C library fopen functions.            An assembly language example follows:                          DB        'foo.bar',0            No spaces are included in the pathname.  Normally            only the file name stem (no directory prefix) is            transmitted unless the sender has selected YAM's f            option to send the full pathname.  The source            drive (A:, B:, etc.) is never sent.       Chapter 13             DRAFT 3-24-86                      17       DRAFT ZMODEM Protocol Ref 02-23-86                        18            Filename Considerations:               o+ File names should be translated to lower case                 unless the sending system supports                 upper/lower case file names.  This is a                 convenience for users of systems (such as                 Unix) which store filenames in upper and                 lower case.               o+ The receiver should accommodate file names in                 lower and upper case.               o+ The rb(1) program on Unix systems normally                 translates the filename to lower case unless                 one or more letters in the filename are                 already in lower case.               o+ When transmitting files between different                 operating systems, file names must be                 acceptable to both the sender and receiving                 operating systems.            If directories are included, they are delimited by            /; i.e., "subdir/foo" is acceptable, "subdir\foo"            is not.       Length The file length and each of the succeeding            fields are optional.1 The length field is stored            as a decimal string counting the number of data            bytes in the file.            With ZMODEM, the receiver uses the file length            only for display (progress reporting) purposes;            the actual length is determined by the data            transfer.       Modification Date A single space separates the            modification date from the file length.            The mod date is optional, and the filename and            length may be sent without requiring the mod date            to be sent.            The mod date is sent as an octal number giving the            time the contents of the file were last changed            measured in seconds from Jan 1 1970 Universal       __________        1. Fields may not be skipped.       Chapter 13             DRAFT 3-24-86                      18       DRAFT ZMODEM Protocol Ref 02-23-86                        19            Coordinated Time (GMT).  A date of 0 implies the            modification date is unknown and should be left as            the date the file is received.            This standard format was chosen to eliminate            ambiguities arising from transfers between            different time zones.            Two Microsoft blunders complicate the use of            modification dates in file transfers with            MSDOS(TM) systems.  The first is the lack of            timezone standardization in MS-DOS.  A file's            creation time can not be known unless the timezone            of the system that wrote the file2 is known.  Unix            solved this problem (for planet Earth, anyway) by            stamping files with Universal Time (GMT).            Microsoft would have to include the timezone of            origin in the directory entries, but does not.            Professional-YAM gets around this problem by using            the z parameter which is set to the number of            minutes local time lags GMT.  For files known to            originate from a different timezone, the -zT            option may be used to specify T as the timezone            for an individual file transfer.            The second problem is the lack of a separate file            creation date in DOS.  Since some backup schemes            used with DOS rely on the file creation date to            select files to be copied to the archive, back-            dating the file modification date could interfere            with the safety of the transferred files.  For            this reason, Professional-YAM does not modify the            date of received files with the header information            unless the d parameter is non zero.       Mode A single space separates the file mode from the            modification date.  The file mode is stored as an            octal string.  Unless the file originated from a            Unix system, the file mode is set to 0.  rb(1)            checks the file mode for the 0x8000 bit which            indicates a Unix type regular file.  Files with            the 0x8000 bit set are assumed to have been sent            from another Unix (or similar) system which uses            the same file conventions.  Such files are not       __________        2. Not necessarily that of the transmitting system!       Chapter 13             DRAFT 3-24-86                      19       DRAFT ZMODEM Protocol Ref 02-23-86                        20            translated in any way.       Serial Number A single space separates the serial            number from the file mode.  The serial number of            the transmitting program is stored as an octal            string.  Programs which do not have a serial            number should omit this field, or set it to 0.            The receiver's use of this field is optional.       The file information is terminated by a null.  If only       the pathname is sent, the pathname will be terminated       by two nulls.  The length of the file information       packet, including the trailing null, must not exceed       1024 bytes; a typical length is less than 64 bytes.       14.  MORE INFORMATION       More information may be obtained by calling       Telegodzilla at 503-621-3746.       UUCP sites can obtain the nroff/troff source to this       file with              uucp omen!/usr/caf/public/zmodem.mm /tmp       A continually updated list of available files is stored       in /usr/spool/uucppublic/FILES.       The following L.sys line calls Telegodzilla (Pro-YAM in       host operation).  Telegodzilla waits for carriage       returns to determine the incoming speed.  If none is       detected, 1200 bps is assumed and a greeting is       displayed.       In response to "Name Please:" uucico gives the Pro-YAM       "link" command as a user name.  The password (Giznoid)       controls access to the Xenix system connected to the       IBM PC's other serial port.  Communications between       Pro-YAM and Xenix use 9600 bps; YAM converts this to       the caller's speed.       Finally, the calling uucico logs in as uucp.       omen Any ACU 1200 1-503-621-3746 se:--se: link ord: Giznoid in:--in: uucp       Chapter 15             DRAFT 3-24-86                      20       DRAFT ZMODEM Protocol Ref 02-23-86                        21       15.  ZMODEM Programs       A demonstration version of Professional-YAM is       available as YAMDEMO.LQR (A SQueezed Novosielski       library).  This may be used to test ZMODEM and YMODEM       implementations.       Unix programs supporting the YMODEM protocol are       available on Telegodzilla in the "upgrade" subdirectory       as RBSB.SHQ (a SQueezed shell archive).  Most Unix like       systems are supported, including V7, Sys III, 4.2 BSD,       SYS V, Idris, Coherent, and Regulus.       A version for VAX-VMS is available in VRBSB.SHQ, in the       same directory.       A CP/M assembly version is available as MODEM76.AQM and       MODEM7.LIB.       Irv Hoff has added YMODEM 1k packets and basic YMODEM       batch transfers to the KMD and IMP series programs,       which replace the XMODEM and MODEM7/MDM7xx series       respectively.  Overlays are available for a wide       variety of CP/M systems.       MEX and MEX-PC also support some of the YMODEM       extensions.       Questions about YMODEM, the Professional-YAM       communications program, and requests for evaluation       copies may be directed to:            Chuck Forsberg            Omen Technology Inc            17505-V Sauvie Island Road            Portland Oregon 97231            Voice: 503-621-3406            Modem: 503-621-3746 Speed: 1200,300            Usenet: ...!tektronix!reed!omen!caf            Compuserve: 70715,131            Source: TCE022       Chapter 15             DRAFT 3-24-86                      21                              CONTENTS        1.  ACKNOWLEDGMENTS....................................   2        2.  ROSETTA STONE......................................   2        3.  YET ANOTHER PROTOCOL, AGAIN?.......................   3        4.  ZMODEM Protocol Design Criteria....................   4            4.1   Throughput...................................   4            4.2   Integrity and Robustness.....................   5            4.3   Ease of use..................................   5            4.4   Ease of implementation.......................   5        5.  PACKETIZATION......................................   5            5.1   Link Escape Encoding.........................   6            5.2   Header Packet Information....................   7            5.3   Binary Header Packet.........................   7            5.4   HEX Header Packet............................   8            5.5   Binary Data Packets..........................   8            5.6   HEX Data Packet..............................   9        6.  PROTOCOL TRANSACTION OVERVIEW......................   9        7.  STREAMING TECHNIQUE................................  12        8.  ATTENTION SEQUENCE.................................  12        9.  PACKET/FRAME TYPES.................................  13            9.1   ZRQRINIT.....................................  13            9.2   ZRINIT.......................................  13            9.3   ZSINIT.......................................  13            9.4   ZACK.........................................  13            9.5   ZFILE........................................  13            9.6   ZSKIP........................................  14            9.7   ZNAK.........................................  14            9.8   ZABORT.......................................  14            9.9   ZFIN.........................................  14            9.10  ZRPOS........................................  14            9.11  ZDATA........................................  14            9.12  ZEOF.........................................  14            9.13  ZFERR........................................  14            9.14  ZCRC.........................................  15            9.15  ZCRYPT.......................................  15            9.16  ZCOMPL.......................................  15       10.  Transaction........................................  15       11.  PERFORMANCE........................................  15                                  - i -       12.  TABLES.............................................  16       13.  ZFILE FRAME FILE INFORMATION.......................  17       14.  MORE INFORMATION...................................  20       15.  ZMODEM Programs....................................  21                                  - ii -                             LIST OF FIGURES       Figure 1.  Protocol Overhead Information................  16       Figure 2.  Transmission Time Comparision................  17       Figure 3.  Y/ZMODEM Header Information usage............  17                                 - iii -